ORDINAUX TRANSFINIS

a = 0
a = suc b
a = lim f ; a[n] = f n
ou
a = 0
a = maj f (majorant des f n) suc b = maj (K b) ; lim f = maj f

0, suc 0 = 1, suc (suc 0) = 2, 3, ... w, suc w = w+1, ... w*2, ... w*w = w^2, ... w^w, ... w^w^w, ... e0
epsilon 0 = w^w^...^w = premier point fixe (numéro 0) de \x.w^x = phi0 = FPE (\x.w^x) 0

FPE f = énumération des points fixes de f :
 FPE f 0 = lim 0, f 0, f (f 0), ...
 FPE f (suc x) = lim suc (FPE f x), f (suc (FPE f x)), ...
 FPE f (lim g) = lim \n.FPE f (g n)

epsilon 1 = lim (epsilon 0)+1, w^((epsilon 0)+1), w^w^((epsilon 0)+1), ... (psofessor Quibb)
        = lim epsilon 0, (epsilon 0) ^ (epsilon 0) = w^w^(epsilon 0)^2, (epsilon 0) ^ (epsilon 0) ^ (epsilon 0) = w^w^w^(epsilon 0)^2, ...
 =w^w^...^w^(epsilon0+1) = second point fixe (numéro 1) de \x.w^x = FPE (\x.w^x) 1
epsilon = \x.epsilon x énumère les points fixes de \x.w^x : epsilon = FPE (\x.w^x)
 epsilon 0 = FPE (\x.w^x) 0
 epsilon 1 = FPE (\x.w^x) 1
 ...

zeta 0 = premier point fixe (numéro 0) de epsilon = FPE epsilon 0 = FPE (FPE (\x.w^x)) 0 = lim epsilon 0, epsilon (epsilon 0), ...
zeta 1 = second point fixe (numéro 1) de epsilon = FPE epsilon 1 = FPE (FPE (\x.w^x)) 1 = lim zeta 0 + 1, epsilon (zeta 0 + 1), ...
zeta = phi2 = FPE eta = FPE (FPE (\x.w^x))

eta 0 = premier point fixe (numéro 0) de zeta
eta = phi3 = FPE zeta = FPE (FPE (FPE (\x.w^x)))

cantor b a = a + w^b
w^x = cantor x 0
 cantor 0 a = suc a
 cantor (suc b) a = fix (cantor b) a
 cantor (lim f) a = lim (\n.cantor (f n) a)
avec fix f x = lim \n.rpt n f x
et rpt n f x = f^n x

phi : Ord -> Ord -> Ord
\x.w^x = phi0 = phi 0
zeta = phi1 = phi 1
eta = phi2 = phi 2
...

http://quibb.blogspot.fr/2012/03/infinity-larger-countable-ordinals.html
"For example, φω(0) is the smallest ordinal that is a fixed point of all the functions φ0, φ1, φ2, etc."

https://en.wikipedia.org/wiki/Veblen_function
http://googology.wikia.com/wiki/Veblen_function
Fundamental sequences for the Veblen hierarchy
For any b, if c is a limit with c < phi b c [?], then let (phi b c)[n] = phi b (c[n])
(phi 0 (c+1))[n] = (phi 0 c ) * n = w^c * n
(phi (b+1) 0)(n] = (phi b)^n 0
(phi (b+1) (c+1))[0] = (phi (b+1) c) + 1, (phi (b+1) (c+1))[n+1] = phi b ((phi (b+1) (c+1))[n])
(phi (b+1) (c+1))[n] = (phi b)^n((phi (b+1) c)+1)
 point fixe de phi b suivant phi (b+1) c
 = lim (phi (b+1) c)+1, phi b ((phi (b+1) c)+1), ...
For b limit :
if b < phi b 0 [?], (phi b 0)[n] = phi (b[n]) 0
(phi b (c+1))[n] = phi (b[n]) ((phi b c) + 1) [?]

phi (lim f) 0 = lim \n.phi (f n) 0 si lim f < phi (lim f) 0 [?]
phi (lim f) (x+1) = lim \n.phi (f n) (x+1) : incorrect ?
phi (lim f) (x+1) = lim \n.phi (f n) (phi (lim f) x + 1) [?]

b limite : phi b (c+1) = lim(n=0,1,2,…) phi b[n] (phi b c + 1)

lim \n. phi (f n) 1
comparer avec
lim \n. phi (f n) (phi (lim f) 0 + 1)
lim \n. phi (f n) (lim \p. phi (f p) 0) + 1)

phi (lim f) (b+1)
au lieu du point fixe (de quoi?) suivant phi (lim f) b
le point fixe suivant lim \n. phi (f n) b
lim \n. (point fixe suivant phi (f n) b)
lim \n. phi (f n) (b+1)

http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf :

φf 0 = f
φf (α + 1) = enumeration of fixed points of φfα
φfλ = enumeration of common fixed points of φfα for all α < λ

zeta énumère les points fixes de epsilon
zeta (x+1) = point fixe de epsilon suivant zeta x
phi 2 (x+1) = point fixe de phi 1 suivant phi 2 x
phi l (x+1) = point fixe de phi m suivant phi l x pour m < l ou m = l[n]
point fixe de f suivant a = lim a+1, f(a+1), f(f(a+1)), …
point fixe de phi l[n] suivant phi l x = lim_n lim phi l x + 1, phi l[n] (phi l x + 1), …
comparer avec:
lim phi l[0] (phi l x + 1), phi l[1] (phi l x + 1), …

phi a 0 = lim phi a[0] 0, phi a[1] 0, …
phi (lim f) 0 = lim \n. phi (f n) 0
normalement phi a 1 = le point fixe suivant phi a 0
remplacer par:
phi (lim f) 1 = lim \n. (le point fixe suivant phi (f n) 0)
        remplacé par phi (f n) 1 ?
 = lim \n. phi (f n) 1
comparer avec
lim \n. phi (f n) (phi (lim f) 0 + 1)
= lim \n. phi (f n) (lim \n.phi (f n) 0 + 1)
phi (lim f) 1 = le second point fixe commun des phi (f n)
premier point fixe commun des phi (f n)
 = lim 1er point fixe commun des phi (f 0) … phi (f 1) …
1er point fixe de phi (f n) = phi (f n + 1) 0
lim \n. phi (f n + 1) 0
phi l 1 [n] = phi (l[n]+1) 0 ?
2e → lim \n. phi (f n + 1) 1

phi a b [n] = phi (a[n]+1) b ?
comparer avec
phi a (b+1) [n] = phi a[n] (phi a b + 1)

phi_g 0 = g
phi_g (a+1) = énumération des points fixes de phi_g a
phi_g (lim f) = énumération des points fixes communs des phi_g b pour tous b < lim f
 ou des phi_g (f n)

énumération des points fixes de phi_g (f n) pour n donné
0 → a0 = lim 0, phi_g (f n) 0, phi_g (f n) (phi_g (f n) 0), …
1 → a1 = lim a0+1, phi_g (f n) (a0+1), …
points fixes communs ?

zeta énumère les points fixes de epsilon
zeta 0 = lim 0, epsilon 0, epsilon (epsilon 0) …
zeta 1 = lim zeta 0 + 1, epsilon (zeta 0 + 1), …

phi 2 énumère les points fixes de phi 1
phi 2 0 = lim 0, phi 1 0, phi 1 (phi 1 0) …
phi 2 1 = lim phi 2 0 + 1, phi 1 (phi 2 0 + 1) …

phi (lim f) énumère les points fixes communs des phi (f n)
phi (lim f) 0 = lim \n. lim 0,phi (f n) 0, phi (f n) (phi (f n) 0) …
 = lim \n. phi (f n + 1) 0
 phi (f n + 1) énumère les points fixes de phi (f n)
 phi (f n + 1) 0 = premier point fixe de phi (f n)

phi (lim f) 0 = lim \n. phi (f n) 0 ?

phi (a+1) énumère les points fixes de phi a
phi (lim f) énumère les points fixes communs des phi (f n)
pour n donné:
phi (f n + 1) énumère les points fixes de phi (f n)
énumération des points fixes communs de phi (f n) :
lim phi (f 0 + 1), phi (f 1 + 1), …
phi (lim f) (b+1) = lim \n. phi (f n) (phi (lim f) b + 1)
phi (lim f) b + 1 : suivant phi (lim f) b
lim \n : point fixe des phi (f n)
pourquoi une seule fois phi (f n) ?

https://sites.google.com/site/largenumbers/home/4-2/fgh_c :

ε1 = lim{ε0+1,ω^(ε0+1),ω^ω^(ε0+1),...}
ε2 = lim{ε1+1,ω^(ε1+1),ω^ω^(ε1+1),...}
ε3 = lim{ε2+1,ω^(ε2+1),ω^ω^(ε2+1),...}
etc.

This gives us a system up to ε# where # can be any non-negative integer. This set is the ordinal ε(ω). The above trick won't work, on ε(ω) itself unfortunately, because ω is a limit ordinal. However, when the input to the epsilon function is a limit ordinal we can define the set with the fundamental sequence for the limit ordinal. ie:
 ε(ω) = lim{ ε0,ε1,ε2,ε3,...}

        With just those two definitions in place we can already get all the way to ordinal ε(0,1)! Some examples:
ε(ω+1) = lim{ε(ω)+1,ω^(ε(ω)+1),ω^ω^(ε(ω)+1),…}
[ phi a (b+1) = lim phi a b + 1, phi a (phi a b + 1), ...]
 ...
ε(ω*2) = lim{ ε(ω),ε(ω+1),ε(ω+2),ε(ω+3),...}
ε(ω*2+1) = lim{ε(ω*2)+1,ω^(ε(ω*2)+1),ω^ω^(ε(ω*2)+1),...}
...
ε(ω2) = lim{ ε0,ε(ω),ε(ω*2),ε(ω*3),...}
...
 ε(ω^ω) = lim{ ε1,ε(ω),ε(ω2),ε(ω3),...}
...
ε(ε0) = lim{ ε1,ε(ω),ε(ω^ω),ε(ω^ω^ω),...}
ε(ε0+1) = lim{ε(ε0)+1,ω^(ε(ε0)+1),ω^ω^(ε(ε0)+1),...}
...
ε(ε(ε0)) = lim{ ε(ε(1)),ε(ε(ω)),ε(ε(ω^ω)),ε(ε(ω^ω^ω)),...}
...

https://sites.google.com/site/largenumbers/home/4-2/fgh_gamma0 :

Whenever the index is a limit ordinal we can observe that φα(0) can be defined as:
φα(0) = φα[0](0) U φα[1](0) U φα[2](0) U ...
        When the argument is a successor ordinal, we can define it as:
φα(β+1) = φα[0](φα(β)+1) U φα[1](φα(β)+1) U φα[2](φα(β)+1) U ...
        What this means in laymen's terms is basically that we take the ordinal φα(β), and we can extend it using any Veblen function φγ , where γ < α.
        If on the other hand the argument to the function is itself a limit ordinal, we can simply take the union of the fundamental sequences as follows:
φα(β) = φα(β[0]) U φα(β[1]) U φα(β[2]) U ...
        Altogether the following definitions can be used to define a much more extended hierarchy of Veblen functions. It is now possible for us to use any ordinal we can so far construct as an index to the function. To make matters easier we can also adopt the binary Veblen notation:
φ(α,β) = φα(β)
        We can now construct ordinals such as:
φ(ω+1,0) , φ(ω+2,0), ... φ(ω*2,0), φ(ω*3,0), ... ,φ(ω2,0), φ(ω3,0), ... ,φ(ωω,0),
... , φ(ε0,0) , φ(ε(ε0),0) , ... ,φ(ζ0,0), ... φ(φ(3,0),0), φ(φ(4,0),0), ...
φ(φ(φ(1,0),0),0), φ(φ(φ(φ(1,0),0),0),0), φ(φ(φ(φ(φ(1,0),0),0),0),0), ...

ε(0,0) --> φ(1,0)
ε(0,1) --> φ(2,0)
ε(0,2) --> φ(3,0)
ε(0,3) --> φ(4,0)
...
ε(0,ω) --> φ(ω,0)
etc.

ε(α+1)[n] = ω^ω^ω^ ... ^ω^ω^(ε(α)+1) /n ω's

Strictly following this rule we have:

ε(ε(0,1)+1)[n] = ω^ω^ω^ ... ^ω^ω^(ε(ε(0,1))+1) /n ω's

Again we get an additional passenger in the form of ε(ε(0,1)), but this is again negligible. We can go further still. As you can imagine we can now create a whole new class of epsilon numbers, which take ε(0,1) into the fold, along with all the construction rules we already established. We get things like ...

ε(ε(0,1)+2),ε(ε(0,1)+3), ... ε(ε(0,1)+ε(0,1)) ... ε(ωε(0,1)+1)

... ε(ε(ε(0,1)+1)), ε(ε(ε(ε(0,1)+1))) ...

This leads to the next fixed point of the function β-->ε(β). This second fixed point is labeled ε(1,1). Furthermore we can give it the following fundamental sequence:

ε(1,1)[0] = ε(0,1)+1

ε(1,1)[n] = ε(ε(1,1)[n-1])

So basically we are nesting ε(0,1)+1 inside the previous epsilon-function to get the next value for our ε(α,1) function. We can then proceed predictably in the following manner:

ε(2,1)[0] = ε(1,1)+1

ε(2,1)[n] = ε(ε(2,1)[n-1])

ε(3,1)[0] = ε(2,1)+1

ε(3,1)[n] = ε(ε(3,1)[n-1])

etc.

        Eventually we hit a limit ordinal in the first argument. Simply let:

ε(ω,1)[n] = ε(n,1)

in general...

ε(λ,1)[n] = ε(λ[n],1)

This covers the ε(β,1) function. Next we define the ε(β,2) function. We begin with:

ε(0,2)[0] = 0

ε(0,2)[n] = ε(ε(0,2)[n-1],1)

ε(0,2) can then be extended via ω^β, ε(β), and even ε(β,1). This will eventually culminate in iteratively plugging in ε(0,2)+1 into function ε(β,1). In this manner we define the next value for our new function:

ε(1,2)[0] = ε(0,2)+1

ε(1,2)[n] = ε(ε(1,2)[n-1],1)

Again we continue in this manner until we hit a limit ordinal...

ε(λ,2)[n] = ε(λ[n],2)

It shouldn't be too hard to imagine how we might construct fundamental sequences, as long as the 2nd argument is < ω. How do we chose a fundamental sequence for ε(0,ω)? Simple ... just take the fundamental sequence of the limit ordinal. ie:

ε(0,ω)[n] = ε(0,n)

in general ...

ε(0,λ)[n] = ε(0,λ[n])

In this manner we can continually create new functions below the ordinal Γ(0). This is still quite informal however. What we want is to generalize these principles into a small set of simple transformations that we can use. Let's now formalize this system for use in FGH.

https://www.physicsforums.com/threads/fundamental-sequences-for-the-veblen-hierarchy-of-ordinals.933538/#post-5898889

Just for the sake of some further clarity on this point (in case one doesn't want to use directly the discussion in the paragraph that follows) .... if we want to verify the following equation (for limit β):
φβ(γ+1)[n]=φβ[n](φβ(γ)+1)
then we just want to show the following two points:
(i) φβ[n](φβ(γ)+1) is a strictly increasing sequence of values (for increasing n).
(ii) sup{φβ[n](φβ(γ)+1)|n∈ω}=φβ(γ+1)
To show (ii) ---- since φβ enumerates all of the common fixed points (in strictly increasing order) of all φα's (where α<β), we can do this by proving the following two facts:
(1) sup{φβ[n](φβ(γ)+1)|n∈ω} is a common fixed point for all φα's (where α<β).
(2) There is no value between φβ(γ) and sup{φβ[n](φβ(γ)+1)|n∈ω} that is a common fixed point for all φα's (where α<β).
(i) seems intuitively plausible to me, and also (2), the less evident is (1), but I have perhaps an idea of a possible proof.
We have to prove that sup{φβ[n](φβ(γ)+1)|n∈ω} is a common fixed point for all φα's (where α<β).
I guess this is the same as proving that it is a common fixed point for all φβ[p] with p∈ω (is it true ?)
Then we have to prove that for any p∈ω, we have :
φβ[p](sup{φβ[n](φβ(γ)+1)|n∈ω})=sup{φβ[n](φβ(γ)+1)|n∈ω}
We have for a given p :
φβ[p](sup{φβ[n](φβ(γ)+1)|n∈ω})
=φβ[p](φβ[0](φβ(γ)+1) ∪ φβ[1](φβ(γ)+1) ∪ ... ∪ φβ[p](φβ(γ)+1) ∪ φβ[p+1](φβ(γ)+1) ∪ ...)
=φβ[p](φβ[0](φβ(γ)+1)) ∪ φβ[p](φβ[1](φβ(γ)+1)) ∪ ... ∪ φβ[p](φβ[p](φβ(γ)+1)) ∪ φβ[p](φβ[p+1](φβ(γ)+1)) ∪ ...
But since we have φα(φβ(γ))=φβ(γ) if α<β, and β[p]<β[p+1], then φβ[p](φβ[p+1](φβ(γ)+1))=(φβ[p+1](φβ(γ)+1), idem for the following terms.
So the previous expression is equivalent to :
φβ[p](φβ[0](φβ(γ)+1)) ∪ φβ[p](φβ[1](φβ(γ)+1)) ∪ ... ∪ φβ[p](φβ[p](φβ(γ)+1)) ∪ φβ[p+1](φβ(γ)+1) ∪ ...
We have to prove it is equal to :
sup{φβ[n](φβ(γ)+1)|n∈ω}=φβ[0](φβ(γ)+1) ∪ φβ[1](φβ(γ)+1) ∪ ... ∪ φβ[p](φβ(γ)+1) ∪ φβ[p+1](φβ(γ)+1) ∪...
These two expressions differs only by the n+1 first terms which are the smallest, the following terms ( φβ[p+1](φβ(γ)+1) and after) are equal. It seems plausible to me that the difference of the first terms does not matter, and that the equality of the following terms which are greater is sufficient for the equality of the complete expressions.

We can observe that:
sup{φβ[n](φβ(γ)+1)|n∈ω}=sup{φα(φβ(γ)+1)|α<β}
Note that this equality uses statement(A) above.
Now fix any arbitrary value(limit or not doesn't matter) λ<β. We want to prove that sup{φα(φβ(γ)+1)|α<β} is a fixed point of φλ. Alternatively:
sup{φα(φβ(γ)+1)|α<β}∈range(φλ+1)
Further we can observe that:
(D)-- range(φα1)⊇range(φα2) whenever α1<α2
Now indeed there is some N∈ω such that:
β[n]≥λ+1 for all n≥N (where n∈ω)
Note that because λ<β and β is a limit, we must have λ+1<β.
Now we can write:
sup{φα(φβ(γ)+1)|α<β}=sup{φα(φβ(γ)+1)|β[N]≤α<β}=sup{φβ[n](φβ(γ)+1)|N≤n<ω}
Observe that the equalities use statement (A).
Now if you observe the sequence of terms:
φβ[N](φβ(γ)+1),φβ[N+1](φβ(γ)+1),φβ[N+2](φβ(γ)+1),φβ[N+3](φβ(γ)+1),......
This is a strictly increasing sequence of values and furthermore every term in this sequence belongs to range(φλ+1)(due to statement-D above). Now let us suppose that:
φλ+1(a0)=φβ[N](φβ(γ)+1)
φλ+1(a1)=φβ[N+1](φβ(γ)+1)
φλ+1(a2)=φβ[N+2](φβ(γ)+1)
and so on....
Now the sequence of values a0,a1,a2,a3.... must form a fundamental sequence (due to φλ+1 being a strictly increasing function). Hence the limit/sup of:
φβ[N](φβ(γ)+1),φβ[N+1](φβ(γ)+1),φβ[N+2](φβ(γ)+1),φβ[N+3](φβ(γ)+1),......
belongs to range(φλ+1) (because φλ+1 is a normal, and hence continuous, function).

(i) φβ[n](φβ(γ)+1) is a strictly increasing sequence of values (for increasing n).

This follows from the statement described next. When β is a limit:
(A)-- φα1(φβ(γ)+1)>φα2(φβ(γ)+1) for any arbitrary α1,α2 where β>α1>α2
More specifically if we can prove for all X<β that:
φα1(φβ(γ)+1)>φα2(φβ(γ)+1) for any arbitrary α1,α2 where X≥α1>α2
then we are done.
We want to prove this by (transfinite) induction. As the base case, what we want to show is:
φ1(φβ(γ)+1)>φ0(φβ(γ)+1)=ω.φβ(γ)+ω
We also know that (by reasoning mentioned in post#2):
φ0(φβ(γ))=φ1(φβ(γ))=φβ(γ)
So we just want to show that there is no value lying between φβ(γ)+1 (inclusive) and φ0(φβ(γ)+1) (inclusive) that is a fixed point of φ0. I think it shouldn't be difficult at all (but probably a bit tedious to write here in detail).
For successor case what we want to prove is:
φα1(φβ(γ)+1)>φα2(φβ(γ)+1) for any arbitrary α1,α2 where α+1≥α1>α2
Our inductive assumption is:
φα1(φβ(γ)+1)>φα2(φβ(γ)+1) for any arbitrary α1,α2 where α≥α1>α2
It should suffice to prove that for any α<β (because proving for all combinations follows rather directly from that):
φα+1(φβ(γ)+1)>φα(φβ(γ)+1)
This should be nearly identical (to base case) because we can observe (somewhat trivially) that for all x,α1,α2:
φα2(x)≥φα1(x) whenever α2≥α1
More specifically, for our purposes I think we can use:
φα(x)≥φ0(x)
So a similar reasoning that we applied in base case can be carried over (with minor change).
For limit case let λ denote some limit value less than β. What we want to prove is:
φα1(φβ(γ)+1)>φα2(φβ(γ)+1) for any arbitrary α1,α2 where λ≥α1>α2
It should suffice to prove that (proving for all combinations should follow directly after this):
φλ(φβ(γ)+1)>φα(φβ(γ)+1) for any arbitrary α<λ
We can show this by contradiction by assuming:
(B) -- φλ(φβ(γ)+1)≤φα(φβ(γ)+1) for "some" α<λ
But we have (proved before):
(C) -- φα+1(φβ(γ)+1)>φα(φβ(γ)+1)
AND (once again by reasoning mentioned in beginning of post#2):
φλ(φβ(γ))=φα(φβ(γ))=φα+1(φβ(γ))=φβ(γ)
This leads to a contradiction because, after the value φβ(γ), the very next fixed point of the function φα must occur after φα(φβ(γ)+1) (otherwise equation(C) wouldn't make any sense).
However, this contradicts with equation(B) (shouldn't be too difficult to see why). That's because every value in range of φλ must be a fixed point of ALL φX's (with X<λ). And yet the value φλ(φβ(γ)+1) isn't a fixed point of φα. Hence our conclusion follows.

https://www.physicsforums.com/threads/fast-growing-hierarchy-beyond-veblen.881440/

Here are few points:
a) Normal Functions
A normal function, say f, has three properties:
1. f(0)>0
2. f must be strictly increasing
3. f must be continuous (value at limits must be equal to least upper bound of all previous values)
A function such as:
f(x)=x.ω
is not normal because it doesn't satisfy any of the three properties above. You only to test values for a small initial interval to see that.
f(x)=ω.x
is not normal because it doesn't satisfy property-1.
However, a slight modification of this function is normal (if you work around a bit, you can identify the function enumerating its fixed points):
f(x)=ω+ω.x
If we switch the terms though it doesn't remain normal. For example:
f(x)=ω.x+ω
isn't normal because it fails to satisfy property-3 (continuity).
b) As you might have read that every normal function has fixed points. Suppose we are given some normal function f. I am sure that one can show generally (I don't know much about rigorous arguments) that the first fixed point of f is limit/least-upper-bound of following sequence:
f(0), f(f(0)), f(f(f(0))), ....
If you denote the x-th fixed point as F(x), for example ..... then the limit of above sequence is F(0). Similarly, I think, F(1) can be given as limit of( re-call that f(F(0))=F(0) ):
f(F(0)+1), f(f(F(0)+1)), f(f(f(F(0)+1))), .....
Because Veblen showed that F is normal, F(ω) would be limit of F(0),F(1),F(2),F(3),.....
Note that first fixed point of epsilon numbers can be written as(I am using square brackers to denote sub-scripting):
ε(0), ε[ε(0)], ε[ε[ε(0)]], ε[ε[ε[ε(0)]]], .....
If you note, this is a special case of the point made above.
c) I think probably if you iterate the process of fixed points for a normal function just finite number of times there would be no problem. However, starting from ω you would have to be careful. At limits the function you will get from a "point-wise supremum" will not be normal for sure. For example, I am quite sure it would stay constant for very large intervals. This will have to be fixed on limits.
Probably this point is a little easier to see if you use the function ω+ω.x (or for that matter 1+x) instead of ω^x.
edit:
I guess it might be worth pointing out one more simpler example for (b). For example, we say that ε0 is first fixed point of f(x)=ω^x. One way is to look at the sequence mentioned in (b). For example:
f(0)=1
f(f(0))=f(1)=ω
f(f(f(0)))=f(ω)=ω^ω
f(f(f(f(0))))=f(ω^ω)=(ω^ω)^ω
and so on…

Implémentations :

#### Ordinal Gamma0 in Coq
Inductive ordinal : Type :=
 | Zero : ordinal
 | Succ : ordinal -> ordinal
 | Limit : (nat -> ordinal) -> ordinal.

Fixpoint iter (a:Type) (f:a->a) (n:nat) (x:a) : a :=
 match n with
  | O => x
  | S p => iter a f p (f x)
 end.

Definition OpLim (F:nat->ordinal->ordinal) (a:ordinal) : ordinal :=
 Limit (fun n => F n a).

Definition OpItw (f:ordinal->ordinal) : ordinal->ordinal :=
 OpLim (iter _ f).

Fixpoint cantor (a:ordinal) (c:ordinal) : ordinal :=
 match c with
  | Zero => Succ a
  | Succ b => OpItw (fun x => cantor x b) a
  | Limit f => Limit (fun n => cantor a (f n))
 end.

Fixpoint Nabla (f:ordinal->ordinal) (b:ordinal) : ordinal :=
 match b with
  | Zero => f Zero
  | Succ a => f (Succ (Nabla f a))
  | Limit h => Limit (fun n => Nabla f (h n))
 end.

Definition deriv (f:ordinal->ordinal) : ordinal->ordinal :=
 Nabla (OpItw f).

Fixpoint veblen (b:ordinal) : ordinal->ordinal :=
 match b with
  | Zero => Nabla (OpLim (iter _ (cantor Zero)))
  | Succ a => Nabla (OpLim (iter _ (veblen a)))
  | Limit f => Nabla (OpLim (fun n => veblen (f n)))
 end.

Definition veb (a:ordinal) : ordinal := veblen a Zero.

Definition epsilon0 : ordinal := veb Zero.

Definition Gamma0 : ordinal := Limit (fun n => iter _ veb n Zero).

Check epsilon0.
Check Gamma0.

http://isabelle.in.tum.de/website-Isabelle2017-RC2/dist/library/HOL/HOL-Induct/Ordinals.html

theory Ordinals
imports Main
(* Title: HOL/Induct/Ordinals.thy
    Author: Stefan Berghofer and Markus Wenzel, TU Muenchen
*)

section ‹Ordinals›

theory Ordinals
imports Main
begin

text ‹
  Some basic definitions of ordinal numbers. Draws an Agda
  development (in Martin-L\"of type theory) by Peter Hancock (see
  ?â¹http://www.dcs.ed.ac.uk/home/pgh/chat.html›).
›

datatype ordinal =
    Zero
  | Succ ordinal
  | Limit "nat ⇒ ordinal"

primrec pred :: "ordinal ⇒ nat ⇒ ordinal option"
where
  "pred Zero n = None"
| "pred (Succ a) n = Some a"
| "pred (Limit f) n = Some (f n)"

abbreviation (input) iter :: "('a ⇒ 'a) ⇒ nat ⇒ ('a ⇒ 'a)"
  where "iter f n ≡ f ^^ n"

definition OpLim :: "(nat ⇒ (ordinal ⇒ ordinal)) ⇒ (ordinal ⇒ ordinal)"
  where "OpLim F a = Limit (λn. F n a)"

definition OpItw :: "(ordinal ⇒ ordinal) ⇒ (ordinal ⇒ ordinal)" ("⨆")
  where "⨆f = OpLim (iter f)"

primrec cantor :: "ordinal ⇒ ordinal ⇒ ordinal"
where
  "cantor a Zero = Succ a"
| "cantor a (Succ b) = ⨆(λx. cantor x b) a"
| "cantor a (Limit f) = Limit (λn. cantor a (f n))"

primrec Nabla :: "(ordinal ⇒ ordinal) ⇒ (ordinal ⇒ ordinal)" ("∇")
where
  "∇f Zero = f Zero"
| "∇f (Succ a) = f (Succ (∇f a))"
| "∇f (Limit h) = Limit (λn. ∇f (h n))"

definition deriv :: "(ordinal ⇒ ordinal) ⇒ (ordinal ⇒ ordinal)"
  where "deriv f = ∇(⨆f)"

primrec veblen :: "ordinal ⇒ ordinal ⇒ ordinal"
where
  "veblen Zero = ∇(OpLim (iter (cantor Zero)))"
| "veblen (Succ a) = ∇(OpLim (iter (veblen a)))"
| "veblen (Limit f) = ∇(OpLim (λn. veblen (f n)))"

definition "veb a = veblen a Zero"
definition "ε⇩0 = veb Zero"
definition "Γ⇩0 = Limit (λn. iter veb n Zero)"

end

http://www.dcs.ed.ac.uk/home/pgh/ordinals.agda

--#include "amenities.agda"
--#include "naturals.agda"

{- This package assembles together things that
   are connected with the Gentzen lens, for
   the datatype of formal ordinals -}

package Ordinals where

  open Amenities use
     Pi, implies , and,
     N1, N0

  open Naturals use
     Nat, It, Rec, Seq

  Ord :: Set = data O
        | S (a :: Ord)
        | L (ls :: (n :: Nat)->Ord)

  {- Some less barbarous notation -}
  zero :: Ord = O@Ord
  succ :: Ord -> Ord = S@Ord
  limit :: (Nat -> Ord) -> Ord = L@Ord

  {------ The transition structure on Ord ---}

  {- Cofinality -}
  C (a :: Ord) :: Set
    = case a of
        (O) -> N0
        (S a') -> N1
        (L ls) -> Nat

  {- Predecessor -}
  pd (a :: Ord) (t :: C a) :: Ord
    = case a of
        (O) -> case t of { }
        (S a') -> a'
        (L ls) -> ls t

  {--------- operations from Ords to Ords ------------}

  Op :: Set = Ord -> Ord

  {- Composing operations -}
  Comp :: Op -> Op -> Op
     = \(f :: Op) -> \(g :: Op) -> \(a :: Ord) ->
       f (g a)

  {- Iterating operations, to get a sequence -}
  OpIt :: Op -> Seq Op
     = It Ord

  {- pointwise limit of a seuence of operations -}
  OpLim :: Seq Op -> Op
     = \(fs :: Nat -> Op) -> \(a :: Ord) ->
       limit (\(n :: Nat) -> fs n a)

  {- omega iterating an operation -}
  OpItw :: Op -> Op
     = \(f :: Op) -> OpLim (OpIt f)

  {------------ Cantor hierarchy -------------------}

  {- recursive (in second argument). -}
  w :: Ord -> Ord -> Ord
     = \(a :: Ord) ->
       \(b :: Ord) ->
        case b of
        (O) -> succ a
        (S b') -> OpItw (\(x :: Ord) -> x `w` b') a
        (L ls) -> limit (\(n :: Nat) -> a `w` (ls n))

  {- The function a |-> w^a -}
  wexp :: Op = w zero

  {-------- Things related to the Veblen hierarchy --------}

  {- \a -> (f.(+1))^a (f 0) : an essential part of derivative -}
  {- recursive. -}
  Nabla :: Op -> Op
     = \(f :: Op) -> \(a :: Ord) ->
       case a of
        (O) -> f zero
        (S a') -> f (succ (Nabla f a'))
        (L ls) -> limit (\(n :: Nat) -> Nabla f (ls n))

  {- derivative of a normal function -}
  deriv :: Op -> Op
     = \(f :: Op) -> Nabla (OpItw f)

  {- derivative of a sequence of normal function -}
  derivl :: (Nat -> Op) -> Op
     = \(sf :: Nat -> Op) -> Nabla (OpLim sf)

  {- Veblen hierarchy -}
  {- recursive -}
  v :: Ord -> Ord -> Ord
     = \(a :: Ord) ->
        let { pds :: Seq Op =
        case a of
        (O) -> OpIt (w a)
        (S a') -> OpIt (v a')
        (L ls) -> \(n :: Nat) -> v (ls n)
        } in Nabla (OpLim pds)

  veb :: Op
    = \(a :: Ord) -> v a zero

  {-------- The landmark ordinals ------------}

  epsilon0 :: Ord = veb zero

  Gamma0 :: Ord = limit (\ (n :: Nat) ->
      It Ord veb n zero)

https://hal.inria.fr/hal-00911710/document

http://www.dcs.ed.ac.uk/home/pgh/lenses_paper.ps

http://www.dcs.ed.ac.uk/home/pgh/lenses_talk.ps

http://www.dcs.ed.ac.uk/home/pgh/lenses_talk2.ps

#### Ordinal Gamma0 in Agda
module ordi where

 data nat : Set where
  O : nat
  S : nat -> nat

 data ordinal : Set where
  Zero : ordinal
  Succ : ordinal -> ordinal
  Limit : (nat -> ordinal) -> ordinal

 iter : (a : Set) (f : a -> a) (n : nat) (x : a) -> a
 iter a f O x = x
 iter a f (S p) x = iter a f p (f x)

 OpLim : (nat -> ordinal -> ordinal) -> ordinal -> ordinal
 OpLim F a = Limit (\n -> F n a)

 OpItw : (ordinal -> ordinal) -> ordinal -> ordinal
 OpItw f = OpLim (iter _ f)

 cantor : ordinal -> ordinal -> ordinal
 cantor a Zero = Succ a
 cantor a (Succ b) = OpItw (\x -> cantor x b) a
 cantor a (Limit f) = Limit (\n -> cantor a (f n))

 Nabla : (ordinal -> ordinal) -> ordinal -> ordinal
 Nabla f Zero = f Zero
 Nabla f (Succ a) = f (Succ (Nabla f a))
 Nabla f (Limit h) = Limit (\n -> Nabla f (h n))

 deriv : (ordinal -> ordinal) -> ordinal -> ordinal
 deriv f = Nabla (OpItw f)

 veblen : ordinal -> ordinal -> ordinal
 veblen Zero = Nabla (OpLim (iter _ (cantor Zero)))
 veblen (Succ a) = Nabla (OpLim (iter _ (veblen a)))
 veblen (Limit f) = Nabla (OpLim (\n -> veblen (f n)))

 veb : ordinal -> ordinal
 veb a = veblen a Zero

 epsilon0 : ordinal
 epsilon0 = veb Zero

 Gamma0 : ordinal
 Gamma0 = Limit (\n -> iter _ veb n Zero)

iter a f n x = f^n(x)

OpLim = Lim1

OpItw = H

cantor a b = a + w^b

Nabla f n = (f o suc)^n(f(0))

deriv f n = Nabla (H f) n = ((H f) o suc)^n (H f 0)
deriv f énumère les points fixes de f

veblen a b = phi(1+a,b)

veblen 0 n
 = Nabla (OpLim (iter _ [w^*]))
 = ((OpLim (iter _ [w^*])) o suc)^n (OpLim (iter _ [w^*]) 0)
 = ((OpLim (iter _ [w^*])) o suc)^n (Lim \p. iter _ [w^*] p 0)
 = ((OpLim (iter _ [w^*])) o suc)^n (Lim \p. [w^*]^p 0)
 = ((OpLim (iter _ [w^*])) o suc)^n (H [w^*] 0)
 = ((OpLim (iter _ [w^*])) o suc)^n (epsilon 0)
n = 0 : epsilon 0
n = 1 : OpLim (iter _ [w^*]) (epsilon 0 + 1)
 = Lim \p. iter _ [w^*] p (epsilon 0 + 1)
 = H [w^*] (epsilon 0 + 1)
 = epsilon 1
veblen 0 a = epsilon a

veblen 1 n
 = Nabla (OpLim (iter _ (veblen 0)))
 = Nabla (OpLim (iter _ [epsilon *]))
 = Nabla (OpLim (iter _ epsilon))
veblen 1 0 = H epsilon 0 = zeta 0
veblen 1 = zeta

veblen w 0 = phi(w,0)
 = Nabla (OpLim [veblen *]) 0
 = Nabla (OpLim veblen) 0
 = OpLim veblen 0
 = lim \n. veblen n 0
veblen w 1
 = Nabla (OpLim veblen) 1
 = OpLim veblen (suc (lim \n. veblen n 0))
 = OpLim veblen (phi(w,0)+1)
 = lim \n. veblen n (phi(w,0)+1)

cf https://en.wikipedia.org/wiki/Veblen_function :

Now suppose b that b is a limit :
(…)
For phi_b(c+1), use phi_b(c+1)[n] = phi_b[n](phi_b(c)+1)

phi (lim f) (b+1) = lim \n phi (f n) (phi (lim f) b + 1)
avec f = I et b = 0 :
phi w 1 = lim \n. phi n (phi w 0 + 1)

Generalisation de phi(a,b) :
 - nombre fini de variables : phi (an, …, a1, a0) = phi (n:an, …, 1:a1, 0:a0)
 - nombre transfini de variables : phi (a1:b1, a2:b2, …, an:bn)

Liens :

https://en.wikipedia.org/wiki/Veblen_function

http://googology.wikia.com/wiki/Ordinal_notation

      A. φ(00,01,…,1α+1)=sup≺{φ(00,01,…,xα):x∈On}.
B. φ(00,01,…,1α)=sup≺{φ(00,01,…,1β):β<α} where α∈Lim
C. φ((x+1)0,y1,…,zβ)≻φ(x0,…,zβ), and there is no array between them
D. φ(00,…,(x+1)α+1,…,yβ)=sup≺{φ(00,…,(x+1)α,xα+1,…,yβ)}
E. φ(00,…,xα+1,yα+2,…,zβ)=sup≺{φ(00,…,wα+1,yα+2,…,zβ):w<x} where x∈Lim
F. φ(00,…,(x+1)α,…,yβ)=sup≺{φ(00,…,1γ,…,xα,…,yβ):γ<α} where α∈Lim
G. φ(00,…,xα,…,yβ)=sup≺{φ(00,…,zα,…,yβ):z<x} where x,α∈Lim
http://quibb.blogspot.fr/2012/03/infinity-impredicative-ordinals.html

http://www.ams.org/journals/tran/1908-009-03/S0002-9947-1908-1500814-9/S0002-9947-1908-1500814-9.pdf

Au delà de phi avec un nombre transfini de variables

https://www.physicsforums.com/threads/how-can-we-construct-ordinals-after-large-veblen.934141/

We start with the large Veblen ordinal (LVO) which is the least fixed point of the function α↦φ(1_α), φ(1_α) representing the application of φ with transfinitely many variables with 1 at position α and 0 anywhere else. Then we consider a function F which enumerates the fixed points of α↦φ(1_α). So we have LVO = F(0). The next fixed point F(1) is the limit of LVO+1,φ(1_LVO+1),φ(1_φ(1_LVO+1)),...
Then we can consider the fixed points of the function F and define a function G which enumerates these fixed points, then a function H which enumerates the fixed points of G, and so on.
This construction is similar to ϵ which enumerates the fixed points of α↦ωα, ζ which enumerates the fixed points of ϵ, η which enumerates the fixed points of ζ.
Like we have defined :
- φ0(α)=ωα
- φ1(α)=ϵ(α)
- φ2(α)=ζ(α)
- φ3(α)=η(α)
...
we can define :
- φ′0(α)=φ(1_α)
- φ′1(α)=F(α)
- φ′2(α)=G(α)
- φ′3(α)=H(α)
With this notation we can write LVO=φ′0(0).
Then φ′α(β) can be written as a binary function φ′(α,β) which can be generalized to finitely many variables like φ′(α,β,γ) and transfinitely many variables like φ′(1ω).
Then we can consider the fixed points of the function α↦φ′(1α) and define a function φ′′0 which enumerates these fixed points.
The same way we can define φ′′′, φ′′′′, ...
We can then introduce a new notation :
- Φ0=φ
- Φ1=φ′
- Φ2=φ′′
...
Then we can go on with for example the fixed points of α↦Φα(1α) or something like that ...

Correspondance notations:
 phi(1_a) = phi(a:1)
 phi'0 = alv0
 phi'1 = alv1
 phi'2 = alv2
 …

There is another way to express my construction, using Veblen functions indiced by the function used for φ0.
As SSequence noticed in https://www.physicsforums.com/threa...-for-the-veblen-hierarchy-of-ordinals.933538/ , there are different conventions for φ0(x), like ωx or ϵx. We can write explicitely the convention chosen for φ0 by writing "φf(α,β)" for "φα(β) with function f used for φ0". With this notation we have:
- φ_f(0,β)=f(β)
- φ__f(α+1,β)=(1+β)th fixed point of the function β↦φf(α,β)
- φf(λ,β)=(1+β)th common fixed point of the function β↦φ_f(α,β) for all α<λ, if λ is a limit ordinal.
( See http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf )
Then we generalize the binary function φf(α,β) to finitely many variables: for example φ_f(1,0,α)=(1+α)th common fixed point of the function ξ↦φ(ξ,0) ( see https://en.wikipedia.org/wiki/Veblen_function ) and to infinitely many variables with a finite number of them different from 0, for example φ_f(1_ω).
Then we can define new φ functions by taking for φ0 the function ξ↦φ_f(1_ξ) and define functions φ_ξ↦φf(1ξ) with 2 variables, with finitely many variables and with transfinitely many variables.
To make a correspondence with my previous construction, if f is the function ξ↦ω^ξ, then φ_f(α,β) corresponds to what I wrote φ_α(β), and φ_ξ↦φf(1ξ)(α,β) to φ′_α(β).
If we define the function S by S(f)(ξ)=φ_f(1_ξ), then φ_ξ↦φf(1ξ) can be written φ_S(f). We can then consider φ_S(S(f)) and so on.
Given an ordinal α, we can iterate transfinitely "α times" the application of S to an initial function f0, for example f0(ξ)=ω^ξ, to obtain a function which I will write S^α(f0). We can use this function to define a function φ_S^α(f0) which permits to construct big ordinals.
We must verify that this function really permits to get greater and greater ordinals and does not get stucked in a loop, perhaps by verifying it is "fruitful" or "helpful" in the sense of http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf:
"An ordinal function f∈Ord' is fruitful if it is inflationary, monotone, continuous, and big. Let Fruit be the class of fruitful functions.
An ordinal function h∈Ord' is helpful if it is strictly inflationary, monotone, and strictly big. Let Help be the class of helpful functions."
If it is the case and if this construction is correct, there is probably a correspondence with the notations using ordinal collapsing functions, but for the moment I don't see how to establish it.
And after ? The next step could perhaps start by enumerating the fixed points of a function like ξ↦φ_S^ξ(1_ξ) or something like that ...

(x : ordinal)

De même que :
 epsilon = phi_1 énumère les points fixes de \x.w^x
 zeta = phi_2 énumère les points fixes de epsilon
 …
 epsilon x = phi_1 x = phi(1,x) = phi(1:1,0:x)
 zeta x = phi₂ x = phi(2,x) = phi(1:2,0:x)
 …
on a :
alv0 énumère les points fixes de \a.phi(a:1) :
 alv0 0 = large Veblen = lim 0, phi(0:1), phi(phi(0:1):1), …
 alv0 1 = lim alv0 0 + 1, phi(alv0 0 + 1:1), ...
alv1 énumère les points fixes de alv0 :
 alv1 0 = lim 0, alv0 0, alv0 (alv0 0), ...
…
alv0 x = Phi1(0,x) = Phi1(x) = Phi1(0:x)
alv1 x = Phi1(1,x) = Phi1(1:1,0:x)
…
alvord a x = Phi1(1:a,0:x)
alv0 = alvord 0, alv1 = alvord 1, …
inc0 = incord 0 = \x.w^x
 incord 0 x = w^x
phi = Phi0 = Phiord 0 = Phiinc inc0
inc1 = incord 1 = alvph phi
 inc1 x = incord 1 x = alvph phi x = alvph (Phiinc increase) x
  = alv0 x = Phi1(x) = Phi1(0:x)
  = 1+x ème point fixe de \x.phi(x:1)
Phi1 = Phiord 1 = Phiinc inc1
…
alvph f x = 1+x ème point fixe de \x.f(x:1)

inc0 = incord 0 = increase = \x.w^x
 → phi = Phi0 = Phiord 0 = Phiinc inc0
    - w^x = phi(1:0,0:x)
    - epsilon x = phi(1:1,0:x)
    - zeta x = phi(1:2,0:x)
    …
inc1 = incord 1 = alvph phi = alvphi Phi0
 → Phi1 = Phiord 1 = Phiinc inc1
    - alv0 x = phi1(0:x,1:0)
    - alv1 x = phi1(0:x,1:1)
    …
inc2 = incord 2 = alvphi Phi1
 → Phi2 = Phiord 2 = Phiinc inc2
    …

{-
   A definition of the large Veblen ordinal and after in Agda
   by Jacques Bailhache, March 2016

   See https://en.wikipedia.org/wiki/Veblen_function

    (1) φ(α)=ω**α for a single variable,

    (2) φ(0,αn−1,…,α0)=φ(αn−1,…,α0), and

    (3) for α>0, γ↦φ(αn,…,αi+1,α,0,…,0,γ) is the function enumerating the common fixed points of the functions ξ↦φ(αn,…,αi+1,β,ξ,0,…,0) for all β<α.

    (4) Let α be a transfinite sequence of ordinals (i.e., an ordinal function with finite support) which ends in zero (i.e., such that α₀=0), and let α[0↦γ] denote the same function where the final 0 has been replaced by γ. Then γ↦φ(α[0↦γ]) is defined as the function enumerating the common fixed points of all functions ξ↦φ(β) where β ranges over all sequences which are obtained by decreasing the smallest-indexed nonzero value of α and replacing some smaller-indexed value with the indeterminate ξ (i.e., β=α[ι₀↦ζ,ι↦ξ] meaning that for the smallest index ι₀ such that αι₀ is nonzero the latter has been replaced by some value ζ<αι₀ and that for some smaller index ι<ι₀, the value αι=0 has been replaced with ξ).

-}

module ordalvn where

 data Nat : Set where
  O : Nat
  1+ : Nat -> Nat

 data Ord : Set where
  Zero : Ord
  Suc : Ord -> Ord
  Lim : (Nat -> Ord) -> Ord

 -- rpt n f x = f^n(x)
 rpt : {t : Set} -> Nat -> (t -> t) -> t -> t
 rpt O f x = x
 rpt (1+ n) f x = rpt n f (f x)

 -- smallest fixed point of f greater than x, limit of x, f x, f (f x), ...
 fix : (Ord -> Ord) -> Ord -> Ord
 fix f x = Lim (\n -> rpt n f x)

 w = fix Suc Zero -- not a fixed point in this case !

 -- cantor b a = a + w^b
 cantor : Ord -> Ord -> Ord
 cantor Zero a = Suc a
 cantor (Suc b) a = fix (cantor b) a
 cantor (Lim f) a = Lim (\n -> cantor (f n) a)

 -- increase a = w^a
 increase : Ord -> Ord
 increase a = cantor a Zero

 -- Another possible increase function
 -- this gives a phi function which grows slower
{-
 increase : Ord -> Ord
 increase Zero = Suc Zero
 increase (Suc a) = Suc (increase a)
 increase (Lim f) = Lim (\n -> increase (f n))
-}

 -- Associative list of ordinals
 infixr 40 _=>_&_
 data OrdAList : Set where
  Zeros : OrdAList
  _=>_&_ : Ord -> Ord -> OrdAList -> OrdAList

{-
 phiinc : (Ord -> Ord) -> OrdAList -> Ord
 phiinc inc Zeros = inc Zero -- (1) phi(0) = w**0 = 1
 phiinc inc (Zero => a & Zeros) = inc a -- (1) phi(a) = w**a
 phiinc inc ( k => Zero & al) = phiinc inc al -- eliminate unnecessary Zero value
 phiinc inc (Zero => a & k => Zero & al) = phiinc inc (Zero => a & al) -- idem
 phiinc inc (Zero => a & Zero => b & al) = phiinc inc (Zero => a & al) -- should not appear but necessary for completeness
 phiinc inc (Zero => Lim f & al) = Lim (\n -> phiinc inc (Zero => f n & al)) -- canonical treatment of limit
 phiinc inc ( k => Lim f & al) = Lim (\n -> phiinc inc (k => f n & al)) -- idem
 phiinc inc (Zero => a & k => Lim f & al) = Lim (\n -> phiinc inc (Zero => a & k => f n & al)) -- idem
 phiinc inc ( Suc k => Suc b & al) = fix (\x -> phiinc inc (k => x & Suc k => b & al)) Zero -- (3) least fixed point
 phiinc inc (Zero => Suc a & Suc k => Suc b & al) = fix (\x -> phiinc inc (k => x & Suc k => b & al)) (Suc (phiinc inc (Zero => a & Suc k => Suc b & al))) -- (3) following fixed points
 phiinc inc ( Lim f => Suc b & al) = Lim (\n -> fix (\x -> phiinc inc (f n => x & Lim f => b & al)) Zero) -- (4) least fixed point
 phiinc inc (Zero => Suc a & Lim f => Suc b & al) = Lim (\n -> fix (\x -> phiinc inc (f n => x & Lim f => b & al)) (Suc (phiinc inc (Zero => a & Lim f => Suc b & al)))) -- (4) following fixed points
-}

 phiinc : (Ord -> Ord) -> OrdAList -> Ord
 phiinc inc Zeros = inc Zero -- (1) phi(0) = w**0 = 1
 phiinc inc (Zero => a & Zeros) = inc a -- (1) phi(a) = w**a
 phiinc inc ( k => Zero & al) = phiinc inc al -- eliminate unnecessary Zero value
 phiinc inc (Zero => a & k => Zero & al) = phiinc inc (Zero => a & al) -- idem
 phiinc inc (Zero => a & Zero => b & al) = phiinc inc (Zero => a & al) -- should not appear but necessary for completeness
 phiinc inc (Zero => Lim f & al) = Lim (\n -> phiinc inc (Zero => f n & al)) -- canonical treatment of limit
 phiinc inc ( Suc k => Suc b & al) = fix (\x -> phiinc inc (k => x & Suc k => b & al)) Zero -- (3) least fixed point
 phiinc inc (Zero => Suc a & Suc k => Suc b & al) = fix (\x -> phiinc inc (k => x & Suc k => b & al)) (Suc (phiinc inc (Zero => a & Suc k => Suc b & al))) -- (3) following fixed points
 phiinc inc ( Suc k => Lim f & al) = Lim (\n -> phiinc inc (Suc k => f n & al)) -- idem
 -- phiinc inc ( Suc k => Lim f & al) = Lim (\n -> fix (\x -> phiinc inc (k => x & Suc k => f n & al)) Zero) -- idem
 phiinc inc (Zero => Suc a & Suc k => Lim f & al) = Lim (\n -> phiinc inc (k => Suc (phiinc inc (Zero => a & Suc k => Lim f & al)) & Suc k => f n & al)) -- idem
 -- phiinc inc (Zero => Suc a & Suc k => Lim f & al) = Lim (\n -> phiinc inc (Zero => Suc a & k => Suc (phiinc inc (Zero => a & Suc k => Lim f & al)) & Suc k => f n & al)) -- idem
 -- phiinc inc (Zero => Suc a & Suc k => Lim f & al) = Lim (\n -> fix (\x -> phiinc inc (k => x & Suc k => f n & al)) (Suc (phiinc inc (Zero => a & Suc k => Lim f & al)))) -- idem
 phiinc inc ( Lim f => Suc b & al) = Lim (\n -> fix (\x -> phiinc inc (f n => x & Lim f => b & al)) Zero) -- (4) least fixed point
 phiinc inc (Zero => Suc a & Lim f => Suc b & al) = Lim (\n -> fix (\x -> phiinc inc (f n => x & Lim f => b & al)) (Suc (phiinc inc (Zero => a & Lim f => Suc b & al)))) -- (4) following fixed points
 phiinc inc ( Lim f => Lim g & al) = Lim (\n -> phiinc inc (Lim f => g n & al))
 phiinc inc (Zero => Suc a & Lim f => Lim g & al) = Lim (\n -> phiinc inc (f n => phiinc inc (Zero => a & Lim f => Lim g & al) & Lim f => g n & al))
 -- phiinc inc (Zero => Suc a & Lim f => Lim g & al) = Lim (\n -> phiinc inc (Zero => a & Lim f => g n & al))

 -- Usage : phi al, where al is the associative list of couples index => value ordered by increasing values,
 -- absent indexes corresponding to Zero values

 phi = phiinc increase

 SmallVeblen = phi (w => Suc Zero & Zeros)

 LargeVeblen = fix (\x -> phi (x => Suc Zero & Zeros)) Zero

 alv0 : Ord -> Ord
 alv0 Zero = fix (\x -> phi (x => Suc Zero & Zeros)) Zero -- Large Veblen
 alv0 (Suc a) = fix (\x -> phi (x => Suc Zero & Zeros)) (Suc (alv0 a))
 alv0 (Lim f) = Lim (\n -> alv0 (f n))

 alv1 : Ord -> Ord
 alv1 Zero = fix (\x -> alv0 x) Zero
 alv1 (Suc a) = fix (\x -> alv0 x) (Suc (alv1 a))
 alv1 (Lim f) = Lim (\n -> alv1 (f n))

 -- alv1 x = phi1 (Zero => x & Suc Zero => Suc Zero & Zeros)

 phi1 = phiinc alv0

{-
 alvph : (OrdAList -> Ord) -> Ord -> Ord
 alvph ph Zero = fix (\x -> ph (x => Suc Zero & Zeros)) Zero
 alvph ph (Suc a) = fix (\x -> ph (x => Suc Zero & Zeros)) (Suc (alvph ph a))
 alvph ph (Lim f) = Lim (\n -> alvph ph (f n))
-}

 incphi : (OrdAList -> Ord) -> Ord -> Ord
 incphi ph Zero = fix (\x -> ph (x => Suc Zero & Zeros)) Zero
 incphi ph (Suc a) = fix (\x -> ph (x => Suc Zero & Zeros)) (Suc (incphi ph a))
 incphi ph (Lim f) = Lim (\n -> incphi ph (f n))

 -- phi = phiinc increase
 phi1' = phiinc (incphi phi)

 phiord : Ord -> OrdAList -> Ord
 phiord Zero = phiinc increase
 phiord (Suc a) = phiinc (incphi (phiord a))
 phiord (Lim f) = \ph -> Lim (\n -> phiord (f n) ph)

 inc0 = increase
 inc1 = incphi (phiinc inc0)

 incord : Ord -> Ord -> Ord
 incord Zero = increase
 incord (Suc a) = incphi (phiinc (incord a))
 incord (Lim f) = \x -> Lim (\n -> incord (f n) x)

 MyLargeOrdinal = fix (\x -> incord x x) (Suc Zero)

{-
Normally it should terminate because the parameter of phi lexicographically decreases, but Agda is not clever enough to see it,
so it must be called with no termination check option :

$ agda -I --no-termination-check LargeVeblen.agda
        _
   ____ | |
  / __ \ | |
 | |__| |___ __| | ___
 | __ / _ \/ _ |/ __\ Agda Interactive
 | | |/ /_\ \/_| / /_| \
 |_| |\___ /____\_____/ Type :? for help.
        __/ /
        \__/

The interactive mode is no longer supported. Don't complain if it doesn't work.
Checking LargeVeblen (/perso/ord/LargeVeblen.agda).
Finished LargeVeblen.
Main> phi Zeros
Suc Zero
Main> phi (Zero => Suc Zero & Zeros)
Lim (λ n → rpt n (λ a → Suc a) Zero)
Main> phi (Zero => Suc (Suc Zero) & Zeros)
Lim
(λ n → rpt n (λ a → Lim (λ n₁ → rpt n₁ (λ a₁ → Suc a₁) a)) Zero)
Main> phi (Suc Zero => Suc Zero & Zeros)
Lim
(λ n →
   rpt n (λ x → phi (Zero => x & Suc Zero => Zero & Zeros)) Zero)
Main>
-}

Notation de Harold Simmons

http://staff.cs.manchester.ac.uk/~hsimmons/
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/papersandnotes.html
http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/FruitHelp.pdf
http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/Fruitful.pdf
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/Derivatives.ps.gz
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/Comparison.ps.gz
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/Applied-l-calc.ps.gz
http://www.cs.man.ac.uk/~hsimmons/TEMP/TieringNotes.pdf
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/SeparationProps.pdf
https://plato.stanford.edu/

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/ordinal-notations.html

Fix f z = f^w(z+1) = H f (suc z) = plus petit point fixe de f > z

Next = Fix [w^*] = « epsilon suivant »

[0] h = Fix (a → h^a 0) ou Fix (a → h^a w)
[1] H h = Fix (a → H^a h 0)
[2] H h g = Fix (a → H^a h w 0)
…
Delta[0] = w
Delta[1] = Next w = epsilon 0
Delta[2] = [0] Next w = plus petit v tel que v = Next^v w

Veb f z = (Fix f)^(1+z) 0 = (1+z)ème point fixe de f
Enm h a = h^(1+a) 0
Veb = Enm o Fix ; [0] = Fix o Enm
Fix o Veb = Fix o Enm o Fix = [0] o Fix
Fix o Veb^a = [0]^a o Fix

Delta[3] = [1] [0] Next w = Gamma 0 = plus petit v tel que v = [0]^v Next w
Delta[4] = [2] [1] [0] Next w
…

Ensuite?

[3] [2] [1] [0] Next w = [3...0] Next w
[w...0] Next w
[w+1...0] Next w = [1] [w...0] Next w
Points fixes de a → [a...0] Next w

module Simmons where

 -- Natural numbers
 data Nat
  = ZeroN
  | SucN Nat

 -- Ordinals
 data Ord
  = Zero
  | Suc Ord
  | Lim (Nat -> Ord)

 -- Ordinal corresponding to a given natural
 ordOfNat ZeroN = Zero
 ordOfNat (SucN n) = Suc (ordOfNat n)

 -- omega
 w = Lim ordOfNat

 lim0 s = Lim s
 lim1 f x = lim0 (\n -> f n x)
 lim2 f x = lim1 (\n -> f n x)

 -- this does not work :
 -- lim ZeroN s = Lim s
 -- lim (SucN p) f = \x -> lim p (\n -> f n x)

 -- f^a(x)
 fpower0 f Zero x = x
 fpower0 f (Suc a) x = f (fpower0 f a x)
 fpower0 f (Lim s) x = Lim (\n -> fpower0 f (s n) x)

 fpower l f Zero x = x
 fpower l f (Suc a) x = f (fpower l f a x)
 fpower l f (Lim s) x = l (\n -> fpower l f (s n) x)

 -- fix f z = least fixed point of f which is > z
 fix f z = fpower lim0 f w (Suc z) -- Lim (\n -> fpower0 f (ordOfNat n) (Suc z))

 -- cantor b a = a + w^b
 cantor Zero a = Suc a
 cantor (Suc b) a = fix (cantor b) a
 cantor (Lim s) a = Lim (\n -> cantor (s n) a)

 -- expw a = w^a
 expw a = cantor a Zero

 -- next a = least epsilon_b > a
 next = fix expw

 -- [0]
 simmons0 h = fix (\a -> fpower lim0 h a Zero)

 -- [1]
 simmons1 h1 h0 = fix (\a -> fpower lim1 h1 a h0 Zero)

 -- [2]
 simmons2 h2 h1 h0 = fix (\a -> fpower lim2 h2 a h1 h0 Zero)

 -- Large Veblen ordinal
 lvo = simmons2 simmons1 simmons0 next w

LET I ^x x
LET Y [[* *] ['* (* *)]]

LET zeron ^z ^s z
LET sucn ^n ^z ^s (s n)

LET zero ^z ^s ^l z
LET suc ^a ^z ^s ^l (s a)
LET lim ^f ^z ^s ^l (l f)

LET insert ^x ^t ^f (t (f x))
LET tuple (Y ^r ^n ^f : n (f I) : ^p ^x : r p : ^t : f : insert x t)

LET ordOfNat (Y ^r ^n : n zero : ^p : suc : r p)

LET w (lim ordOfNat)

LET lim0 lim
LET lim1 ^f ^x (lim0 : ^n : f n x)
LET lim2 ^f ^x (lim1 : ^n : f n x)

LET limn (Y ^r ^p : p lim : ^q ^f ^x : r q : ^n : f n x)

LET fpower (Y ^r ^l ^f ^a ^x : a x (^b : f : r l f b x) (^s : lim : ^n : r l f (s n) x))

LET fix ^f ^z (fpower lim0 f w : suc z)

LET cantor (Y ^r ^b ^a : b (suc a) (^p : fix (r p) a) (^s : lim : ^n : r (s n) a))

LET expw ^a (cantor a zero)

LET next (fix expw)

LET simmons0 ^h (fix ^a : fpower lim0 h a zero)
LET simmons1 ^h1 ^h0 (fix ^a : fpower lim1 h1 a h0 zero)
LET simmons2 ^h2 ^h1 ^h0 (fix ^a : fpower lim2 h2 a h1 h0 zero)

LET simmonsn ^n ^h (tuple n : ^t : fix ^a : t (fpower (limn n) a) zero)

LET lvo (simmons2 simmons1 simmons0 next w)

LET tupleSimmons (Y ^r ^n : n I ^p : insert (simmonsn p) : r p)

LET delta ^n (tupleSimmons n I next w)

LET howard (lim delta)

howard

Beyond Veblen function
We start with the large Veblen ordinal (LVO) which is the least fixed point of the function α↦φ(1_α), φ(1_α) representing the application of φ with transfinitely many variables with 1 at position α and 0 anywhere else. Then we consider a function F which enumerates the fixed points of α↦φ(1_α). So we have LVO = F(0). The next fixed point F(1) is the limit of LVO+1,φ(1_LVO+1),φ(1_φ(1_LVO+1)),...

Then we can consider the fixed points of the function F and define a function G which enumerates these fixed points, then a function H which enumerates the fixed points of G, and so on.

This construction is similar to ϵ which enumerates the fixed points of α↦ωα, ζ which enumerates the fixed points of ϵ, η which enumerates the fixed points of ζ.*

Like we have defined :
φ0(α)=ωα
φ1(α)=ϵ(α)
φ2(α)=ζ(α)
φ3(α)=η(α)
...
we can define :
φ′0(α)=φ(1_α)
φ′1(α)=F(α)
φ′2(α)=G(α)
φ′3(α)=H(α)
...
With this notation we can write LVO=φ′0(0).
Then φ′α(β) can be written as a binary function φ′(α,β) which can be generalized to finitely many variables like φ′(α,β,γ) and transfinitely many variables like φ′(1ω).

Then we can consider the fixed points of the function α↦φ′(1α) and define a function φ′′0 which enumerates these fixed points.

The same way we can define φ′′′, φ′′′′, ...

We can then introduce a new notation :
Φ0=φ
Φ1=φ′
Φ2=φ′′
...
Then we can go on with for example the fixed points of α↦Φα(1α) or something like that ...

There is another way to express this construction, using Veblen functions indiced by the function used for φ0.

There are different conventions for φ0(x), like ωx or ϵx. We can write explicitely the convention chosen for φ0 by writing "φf(α,β)" for "φα(β) with function f used for φ0". With this notation we have:

φ_f(0,β)=f(β)
φ_f(α+1,β)=(1+β)th fixed point of the function β↦φf(α,β)
φ_f(λ,β)=(1+β)th common fixed point of the function β↦φ_f(α,β) for all α<λ, if λ is a limit ordinal.
( See http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf )
Then we generalize the binary function φf(α,β) to finitely many variables: for example φ_f(1,0,α)=(1+α)th common fixed point of the function ξ↦φ(ξ,0) ( see https://en.wikipedia.org/wiki/Veblen_function ) and to infinitely many variables with a finite number of them different from 0, for example φ_f(1_ω).

Then we can define new φ functions by taking for φ0 the function ξ↦φ_f(1_ξ) and define functions φ_ξ↦φ_f(1_ξ) with 2 variables, with finitely many variables and with transfinitely many variables.

To make a correspondence with my previous construction, if f is the function ξ↦ω^ξ, then φ_f(α,β) corresponds to what I wrote φ_α(β), and φ_ξ↦φf(1ξ)(α,β) to φ′_α(β).

If we define the function S by S(f)(ξ)=φ_f(1_ξ), then φ_ξ↦φf(1ξ) can be written φ_S(f). We can then consider φ_S(S(f)) and so on.

Given an ordinal α, we can iterate transfinitely "α times" the application of S to an initial function f0, for example f0(ξ)=ω^ξ, to obtain a function which I will write S^α(f0). We can use this function to define a function φ_S^α(f0) which permits to construct big ordinals.

---

F(0) = least fixed point of a -> phi(a:1) or phi(1_a) = phi(W:1) = phi((1:1):1) = phi (1:1:1)
W=1:1
F(1) = phi(W:1,0:1) = phi(W:1,1) = phi(1:1:1,1) = phi(1:1:1,0:0:1)
F(a) = phi(1:1:1,a)
G(0) = phi(1:1:1,1:1)
G(a) = phi(1:1:1,1:1,0:a)
H(0) = phi(1:1:1,1:2)
H(a) = phi(1:1:1,1:2,0:a)
Phi_1(b,a) = phi'(b,a) = phi(1:1:1,1:b,0:a)
phi'(a:1) = phi(1:1:1,a:1) = phi(1:1:1,W:1) = phi(1:1:1,1:1:1) = phi(1:1:2)
Phi_2(b,a) = phi''(b,a) = phi(1:1:2,1:b,0:a)
least fixed point of a -> phi(1:1:a) = phi(1:1:W) = phi(1:1:(1:1)) = phi(1:2:1)

Generalized ordinals :
 0
 suc Ord
 Lim (Nat -> Ord)
 Ext (Ord -> Ord)
or :
 O
 suc Ord
 Lim (Nat -> Ord)
 Ass Ord Ord Ord or Ord : Ord , Ord
example :
 W = Ass 1 1 0 = 1:1,0
phi can be seen as a collapsing function

psi(f(W)) = phi(H (f o psi) 0)
plus petit point fixe de f = f(W) avec W = 1,0
exemples:
a = phi(a) = phi(0,a) = w^a = epsilon₀
a = phi(W) = phi(1,0)
Taranovsky :
w^a = C(a,0) = 0+w^a
a = w^a = epsilon₀ = C(W,0)

Large Veblen ordinal in Agda

module LargeVeblen where

 data Nat : Set where
  O : Nat
  1+ : Nat -> Nat

 data Ord : Set where
  Zero : Ord
  Suc : Ord -> Ord
  Lim : (Nat -> Ord) -> Ord

 -- rpt n f x = f^n(x)
 rpt : {t : Set} -> Nat -> (t -> t) -> t -> t
 rpt O f x = x
 rpt (1+ n) f x = rpt n f (f x)

 -- smallest fixed point of f greater than x, limit of x, f x, f (f x), ...
 fix : (Ord -> Ord) -> Ord -> Ord
 fix f x = Lim (\n -> rpt n f x)

 w = fix Suc Zero -- not a fixed point in this case !

 -- cantor a b = b + w^a
 cantor : Ord -> Ord -> Ord
 cantor Zero a = Suc a
 cantor (Suc b) a = fix (cantor b) a
 cantor (Lim f) a = Lim (\n -> cantor (f n) a)

 -- phi0 a = w^a
 phi0 : Ord -> Ord
 phi0 a = cantor a Zero

 -- Another possibility is to use phi'0 instead of phi0 in the definition of phi,
 -- this gives a phi function which grows slower
 phi'0 : Ord -> Ord
 phi'0 Zero = Suc Zero
 phi'0 (Suc a) = Suc (phi'0 a)
 phi'0 (Lim f) = Lim (\n -> phi'0 (f n))

 -- Associative list of ordinals
 infixr 40 _=>_&_
 data OrdAList : Set where
  Zeros : OrdAList
  _=>_&_ : Ord -> Ord -> OrdAList -> OrdAList

 -- Usage : phi al, where al is the associative list of couples index => value ordered by increasing values,
 -- absent indexes corresponding to Zero values

 phi : OrdAList -> Ord
 phi Zeros = phi0 Zero -- (1) phi(0) = w**0 = 1
 phi (Zero => a & Zeros) = phi0 a -- (1) phi(a) = w**a
 phi ( k => Zero & al) = phi al -- eliminate unnecessary Zero value
 phi (Zero => a & k => Zero & al) = phi (Zero => a & al) -- idem
 phi (Zero => a & Zero => b & al) = phi (Zero => a & al) -- should not appear but necessary for completeness
 phi (Zero => Lim f & al) = Lim (\n -> phi (Zero => f n & al)) -- canonical treatment of limit
 phi ( Suc k => Suc b & al) = fix (\x -> phi (k => x & Suc k => b & al)) Zero -- (3) least fixed point
 phi (Zero => Suc a & Suc k => Suc b & al) = fix (\x -> phi (k => x & Suc k => b & al)) (Suc (phi (Zero => a & Suc k => Suc b & al))) -- (3) following fixed points
 phi ( Suc k => Lim f & al) = Lim (\n -> phi (Suc k => f n & al)) -- idem
 phi (Zero => Suc a & Suc k => Lim f & al) = Lim (\n -> phi (k => Suc (phi (Zero => a & Suc k => Lim f & al)) & Suc k => f n & al)) -- idem
 phi ( Lim f => Suc b & al) = Lim (\n -> fix (\x -> phi (f n => x & Lim f => b & al)) Zero) -- (4) least fixed point
 phi (Zero => Suc a & Lim f => Suc b & al) = Lim (\n -> fix (\x -> phi (f n => x & Lim f => b & al)) (Suc (phi (Zero => a & Lim f => Suc b & al)))) -- (4) following fixed points
 phi ( Lim f => Lim g & al) = Lim (\n -> phi (Lim f => g n & al))
 phi (Zero => Suc a & Lim f => Lim g & al) = Lim (\n -> phi (f n => phi (Zero => a & Lim f => Lim g & al) & Lim f => g n & al))

 SmallVeblen = phi (w => Suc Zero & Zeros)

 LargeVeblen = fix (\x -> phi (x => Suc Zero & Zeros)) (Suc Zero)

comparaison avec suites fondamentales https://en.wikipedia.org/wiki/Veblen_function

<br>
<br><span style="font-weight: bold;">Taranovsky's C</span>
<p>
C(a,b) is the least element above b that has degree >= a.
<p>
Definition: A degree for a well-ordered set S is a binary relation on S such that
<ul>
<li> Every element c∈S has degree 0S (the least element of S). 0S only has degree 0S.
 <li> For a limit a, c has degree a iff it has every degree less than a.
 <li> For a successor a'=a+1, either of the following holds:
  <ul>
   <li> An element has degree a' iff it is a limit of elements of degree a.
   <li> There is a limit element d ≤ a such that for every c in S, c has degree a' iff it has degree a and either c ≤ d or c is a limit of elements of degree a (or both).
  </ul>
</ul>
Note: The third condition can be equivalently written as ∀a (Ca+1 = lim(Ca) ∨ ∃d ∈ lim(S)∩(a+1) Ca+1 = lim(Ca) ∪ (Ca∩(d+1))), where S is identified with an ordinal (so a+1 consists of ordinals ≤a), Ca is the set of elements that have degree a, and lim is limit points.
<p>
In other terms : Let ηη be an ordinal, and let 0S and let Ld(a,b) be the statement that aa is a limit of ordinals c such that (c,b)∈D. Let D be the following binary relation over η:
<ul>
<li> ∀a<η:(a,0)∈D
<li> ∀a<η:a≠0⇒(0,a)∉D
<li> ∀b∈Lim∪η:(a,b)∈D⇔∀c&lt;b:(a,c)∈D.
<li> ∀b:(a,b)∈D⇔Ld(a,b+1)∀b:(a,b)∈D⇔Ld(a,b+1)
<li> ∀b:∃d∈Lim∪η:d≤b⇒∀c:(c,a+1)∈D⇔(c≤d∨Ld(c,b))
<li> Then C(a,b)=min{c:c∈η∧c>b∧(c,a)∈D}.
</ul>
C(a, b) = b+ω^a iff C(a, b) ≥ a.
<p>
For ordinals in the standard representation written in the postfix form, the comparison is done in the lexicographical order where 'C' < '0' < 'Ω': For example, C(C(0,0),0) &lt; C(Ω, 0) because 000CC &lt; 0ΩC. (This does not hold for non-standard representations of ordinals.)
<p>
Examples of representations of some ordinals :
<ul>
<li> 0 = 0
<li> 1 = C(0,0) = 0+w^0
<li> 2 = C(0,1) = C(0,C(0,0)) = 1 + w^0
<li> w = C(1,0) = 0+w^1
<li> w+1 = C(0,w) = w+w^0
<li> w*2 = C(1,w) = w+w^1
<li> w^2 = C(2,0) = 0+w^2
<li> w^w = C(w,0) = 0+w^w
<li> w^w^w = C(w^w,0) = 0+w^w^w
<li> epsilon_0 = phi(1,0) = C(W,0)
<li> epsilon_1 = phi(1,1) = C(W,C(W,0))
<li> zeta_0 = phi(2,0) = C(C(W,W),0) = C(W*2,0) with W*2 = C(W,W)
<li> zeta_1 = phi(2,1) = C(W*2,C(W*2,0))
<li> eta_0 = phi(3,0) = C(W*3,0) with W*3 = C(W,C(W,W))
<li> Gamma_0 = phi(1,0,0) = C(C(W*2,W),0) = C(W^2,0) with W^2 = C(W*2,W)
</ul>

module LargeVeblen where

 data Nat : Set where
  O : Nat
  1+ : Nat -> Nat

 data Ord : Set where
  Zero : Ord
  Suc : Ord -> Ord
  Lim : (Nat -> Ord) -> Ord

 -- rpt n f x = f^n(x)
 rpt : {t : Set} -> Nat -> (t -> t) -> t -> t
 rpt O f x = x
 rpt (1+ n) f x = rpt n f (f x)

 -- smallest fixed point of f greater than x, limit of x, f x, f (f x), ...
 fix : (Ord -> Ord) -> Ord -> Ord
 fix f x = Lim (\n -> rpt n f x)

 w = fix Suc Zero -- not a fixed point in this case !

 -- cantor a b = b + w^a
 cantor : Ord -> Ord -> Ord
 cantor Zero a = Suc a
 cantor (Suc b) a = fix (cantor b) a
 cantor (Lim f) a = Lim (\n -> cantor (f n) a)

 -- phi0 a = w^a
 phi0 : Ord -> Ord
 phi0 a = cantor a Zero

 -- Another possibility is to use phi'0 instead of phi0 in the definition of phi,
 -- this gives a phi function which grows slower
 phi'0 : Ord -> Ord
 phi'0 Zero = Suc Zero
 phi'0 (Suc a) = Suc (phi'0 a)
 phi'0 (Lim f) = Lim (\n -> phi'0 (f n))

 -- Associative list of ordinals
 infixr 40 _=>_&_
 data OrdAList : Set where
  Zeros : OrdAList
  _=>_&_ : Ord -> Ord -> OrdAList -> OrdAList

 -- Usage : phi al, where al is the associative list of couples index => value ordered by increasing values,
 -- absent indexes corresponding to Zero values

 phi : OrdAList -> Ord
 phi Zeros = phi0 Zero -- (1) phi(0) = w**0 = 1
 phi (Zero => a & Zeros) = phi0 a -- (1) phi(a) = w**a
 phi ( k => Zero & al) = phi al -- eliminate unnecessary Zero value
 phi (Zero => a & k => Zero & al) = phi (Zero => a & al) -- idem
 phi (Zero => a & Zero => b & al) = phi (Zero => a & al) -- should not appear but necessary for completeness
 phi (Zero => Lim f & al) = Lim (\n -> phi (Zero => f n & al)) -- canonical treatment of limit
 phi ( Suc k => Suc b & al) = fix (\x -> phi (k => x & Suc k => b & al)) Zero -- (3) least fixed point
 phi (Zero => Suc a & Suc k => Suc b & al) = fix (\x -> phi (k => x & Suc k => b & al)) (Suc (phi (Zero => a & Suc k => Suc b & al))) -- (3) following fixed points
 phi ( Suc k => Lim f & al) = Lim (\n -> phi (Suc k => f n & al)) -- idem
 phi (Zero => Suc a & Suc k => Lim f & al) = Lim (\n -> phi (k => Suc (phi (Zero => a & Suc k => Lim f & al)) & Suc k => f n & al)) -- idem
 phi ( Lim f => Suc b & al) = Lim (\n -> fix (\x -> phi (f n => x & Lim f => b & al)) Zero) -- (4) least fixed point
 phi (Zero => Suc a & Lim f => Suc b & al) = Lim (\n -> fix (\x -> phi (f n => x & Lim f => b & al)) (Suc (phi (Zero => a & Lim f => Suc b & al)))) -- (4) following fixed points
 phi ( Lim f => Lim g & al) = Lim (\n -> phi (Lim f => g n & al))
 phi (Zero => Suc a & Lim f => Lim g & al) = Lim (\n -> phi (f n => phi (Zero => a & Lim f => Lim g & al) & Lim f => g n & al))

 SmallVeblen = phi (w => Suc Zero & Zeros)

 LargeVeblen = fix (\x -> phi (x => Suc Zero & Zeros)) (Suc Zero)

data Xord
 = Zero
 | Suc Xord
 | Lim (Nat → Xord)
 | Ass Xord Xord Xord
phi (Ass a b c)
abc:numéros lignes code, p = traité partiellement, + = ajouter ligne
000:1,2
00S:2
00L:2
00A:2,3p,4p
0S0:1
0SS
0SL
0SA:3p,4p,7p,9p,11p,13p
0L0:1,5
0LS:5
0LL:5
0LA:3p,4p,5
0A0:1
0AS:+
0AL:+
0AA:3p,4p
S00:2
S0S:2
S0L:2
S0A:2
SS0:6
SSS:6
SSL:6
SSA:6
SL0:8
SLS:8
SLA:8
SA0:+
SAS:+
SAL:+
SAA:+
L00:2
L0S:2
L0L:2
L0A:2
LS0:10
LSS:10
LSL:10
LSA:10
LLO:12
LLS:12
LLL:12
LLA:12
LA0:+
LAS:+
LAL:+
LAA:+
A00:2
AOS:2
A0L:2
A0A:2
AS0:+
ASS:+
ASL:+
ASA:+
AL0:+
ALS:+
ALL:+
ALA:+
AA0:+
AAS:+
AAL:+
AAA:+

Correspondence between Veblen functions and Madore's ψ (psi) collapsing function
To distinguish between the different Veblen functions, let us call φF the Veblen function with finitely many variables, and φT the Veblen function with transfinitely many variables.
φF is a function which, when applied to a list of countable ordinals, gives a countable ordinal. A list of countable ordinals can be seen as a function which, when applied to a natural number, gives a countable ordinal, with the restriction that the result differs from 0 for finitely many integers. If we denote ω the set of natural numbers and Ω the set of countable ordinals, then this can be written : φF:(ω→Ω)→Ω. If we replace α→β by β^α, we get Ω^Ω^ω, and if we apply ψ to it, we get ψ(Ω^Ω^ω), which is the small Veblen ordinal, the least ordinal that cannot be reached using φF.
For φT, the position of a variable is represented by a countable ordinal instead of a natural number, also with the restriction that finitely many variables differ from 0, so we have φT:(Ω→Ω)→Ω. If we replace α→β by β^α, we get Ω^Ω^Ω, and if we apply ψ to it, we get ψ(Ω^Ω^Ω), which is the large Veblen ordinal, the least ordinal that cannot be reached using
If we extrapolate this correspondence, we can define a generalization of the Veblen function whose limit would be ψ(Ω^Ω^Ω^Ω), and the "position" of a variable would be a function which gives a countable ordinal when applied to a countable ordinal, and so on, up to the Howard ordinal, which is the limit of ψ(Ω),ψ(Ω^Ω),ψ(Ω^Ω^Ω),...

 Ass a b c = c,a:b
 phi (0) = w⁰ = 1
 phi (0:a) = w^a
 phi (al, k:0) = phi(al)
 phi (al, k:0, 0:a) = phi (al, 0:a)
 phi (al, 0:b, 0:a) = phi (al, 0:a)
 phi (al, 0:lim s) = lim n → phi (al, 0:s n)
+phi (al, 0:(al1,x:y)) = ?
 phi (al, k+1:b+1) = fix (x → phi (al, k+1:b, k:x)) 0
 phi (al, k+1:b+1, 0:a+1) = fix (x → phi (al, k+1:b, k:x)) (phi (al, k+1:b+1, 0:a) + 1)
 phi (al, k+1:lim s) = lim n → phi (al, k+1:s n)
 phi (al, k+1:lim s, 0:a+1) = lim n → phi (al, k+1:s n, k:phi(al,k+1:lim s,0:a)+1)
+phi (al, k+1:(al1,x:y)) = ?
+phi (al, k+1:(al1,x:y)) = ?
 phi (al, lim s:b+1) = lim n → fix (x → phi (al, lim s:b, s n:x) 0)
 phi (al, lim s:b+1, 0:a+1) = lim n → fix (x → phi (al, lim s:b, s n:x) (phi (al, lim s:b+1, 0:a) + 1)
 phi (al, lim s:lim t) = lim n → phi (al, lim s:t n)
 phi (al, lim s:lim t, 0:a+1) = lim n → phi (al, lim s:t n, f n:phi(al,lim s:lim t,0:a))
+phi (al, (al1,x:y):b+1) = ?
+phi (al, (al1,x:y):b+1, 0:a+1) = ?
+phi (al, (al1,x:y):lim t) = ?
+phi (al, (al1,x:y):lim t, 0:a+1) = ?
+phi (al, (al1,x:y):(al2,u:v)) = ?
+phi (al, (al1,x:y):(al2,u:v), 0:a+1) = ?

https://sites.google.com/site/travelingtotheinfinity/fundamental-sequences-for-extended-veblen-function
correction phi :
 phi (al, lim s:b+1) = lim n → fix (x → phi (al, lim s:b, s n:x) 0)
 phi (al, lim s:b+1, 0:a+1) = lim n → fix (x → phi (al, lim s:b, s n:x) (phi (al, lim s:b+1, 0:a) + 1)
remplacé par
 phi (al, lim s:b+1) = lim n → phi (lim s:b, s n:1)
 phi (al, lim s:b+1, 0:a+1) = lim n → phi (al, lim s:b, s n:phi(al,lim s:b+1,0:a))

 ancienne version
 nouvelle version

 phi : OrdAList -> Ord
 phi Zeros = phi0 Zero -- (1) phi(0) = w**0 = 1
 phi (Zero => a & Zeros) = phi0 a -- (1) phi(a) = w**a
 phi ( k => Zero & al) = phi al -- eliminate unnecessary Zero value
 phi (Zero => a & k => Zero & al) = phi (Zero => a & al) -- idem
 phi (Zero => a & Zero => b & al) = phi (Zero => a & al) -- should not appear but necessary for completeness
 phi (Zero => Lim f & al) = Lim (\n -> phi (Zero => f n & al)) -- canonical treatment of limit
 phi ( Suc k => Suc b & al) = fix (\x -> phi (k => x & Suc k => b & al)) Zero -- (3) least fixed point
 phi (Zero => Suc a & Suc k => Suc b & al) = fix (\x -> phi (k => x & Suc k => b & al)) (Suc (phi (Zero => a & Suc k => Suc b & al))) -- (3) following fixed points
 phi ( Suc k => Lim f & al) = Lim (\n -> phi (Suc k => f n & al)) -- idem
 phi (Zero => Suc a & Suc k => Lim f & al) = Lim (\n -> phi (k => Suc (phi (Zero => a & Suc k => Lim f & al)) & Suc k => f n & al)) -- idem
 phi ( Lim f => Suc b & al) = Lim (\n -> fix (\x -> phi (f n => x & Lim f => b & al)) Zero) -- (4) least fixed point
 phi ( Lim f => Suc b & al) = Lim (\n → phi (f n => (Suc Zero) & Lim f => b & al))
 phi (Zero => Suc a & Lim f => Suc b & al) = Lim (\n -> fix (\x -> phi (f n => x & Lim f => b & al)) (Suc (phi (Zero => a & Lim f => Suc b & al)))) -- (4) following fixed points
 phi (Zero => Suc a & Lim f => Suc b & al) = Lim (\n → phi (f n => phi (Zero => a & Lim f => Suc b & al) & Lim f => b & al))
 phi ( Lim f => Lim g & al) = Lim (\n -> phi (Lim f => g n & al))
 phi (Zero => Suc a & Lim f => Lim g & al) = Lim (\n -> phi (f n => phi (Zero => a & Lim f => Lim g & al) & Lim f => g n & al))
 phi Zeros = increase Zero
 phi (Ass Zero a Zeros) = increase a
 phi (Ass k Zero al) = phi al
 phi (Ass Zero a (Ass k Zero al)) = phi (Ass Zero a al)
 phi (Ass Zero a (Ass Zero b al)) = phi (Ass Zero a al)
 phi (Ass Zero (Lim f) al) = Lim $ \n -> phi $ Ass Zero (f n) al
 phi (Ass (Suc k) (Suc b) al) = fix (\x -> phi $ Ass k x $ Ass (Suc k) b al) Zero
 phi (Ass Zero (Suc a) (Ass (Suc k) (Suc b) al)) = fix (\x -> phi $ Ass k x $ Ass (Suc k) b al) (Suc $ phi $ Ass Zero a $ Ass (Suc k) (Suc b) al)
 phi (Ass (Suc k) (Lim f) al) = Lim $ \n -> phi $ Ass (Suc k) (f n) al
 phi (Ass Zero (Suc a) (Ass (Suc k) (Lim f) al)) = Lim $ \n -> phi $ Ass k (Suc $ phi $ Ass Zero a $ Ass (Suc k) (Lim f) al) $ Ass (Suc k) (f n) al
 phi (Ass (Lim f) (Suc b) al) = Lim $ \n -> fix (\x -> phi $ Ass (f n) x $ Ass (Lim f) b al) Zero
phi (Ass (Lim f) (Suc b) al) = Lim $ \n -> phi $ Ass (f n) (Suc Zero) $ Ass (Lim f) b al

 phi (Ass Zero (Suc a) (Ass (Lim f) (Suc b) al)) = Lim $ \n -> fix (\x -> phi $ Ass (f n) x $ Ass (Lim f) b al) (Suc $ phi $ Ass Zero a $ Ass (Lim f) (Suc b) al)
 phi (Ass Zero (Suc a) (Ass (Lim f) (Suc b) al)) = Lim $ \n -> phi $ Ass (f n) (phi $ Ass Zero a $ Ass (Lim f) (Suc b) al) $ Ass (Lim f) b al
 phi (Ass (Lim f) (Lim g) al) = Lim $ \n -> phi $ Ass (Lim f) (g n) al
 phi (Ass Zero (Suc a) (Ass (Lim f) (Lim g) al)) = Lim $ \n -> phi $ Ass (f n) (phi $ Ass Zero a $ Ass (Lim f) (Lim g) al) $ Ass (Lim f) (g n) al

correspondance notation combinatoire : autre possibilité :
Gamma_0^...^Gamma₀ = R1 (R1;1 H) suc 0 = epsilon_(Gamma_0+1) = phi(1,Gamma_0+1)
zeta_(Gamma_0+1) = R1 R1;1 H suc 0
Gamma₁ = H [R *->2 R1;1 H suc 0] 0
 = R1;2 R1;1 H suc 0
 = R1;2->1 H suc 0
Gamma_a = phi(1,0,a) = R1;a->1 H suc 0
phi(1,1,0) = H [R1 ;*->1 H suc 0] 0 = R2;1 H suc 0
phi(2,0,0) = H [R*;1 H suc 0] 0 = R1,0;1 H suc 0
phi(3,0,0) = R1,0,0;1 H suc 0 ou R2,0;1 H suc 0 ?
SVO = Rw:1;1 H suc 0
LVO = RW:1;1 H suc 0 = R(1,0):1;1 H suc 0 = R1:1:1;1 H suc 0
BHO = R1:…:1;1 H suc 0

Correspondence between Veblen functions and Madore's ψ (psi) collapsing function
To distinguish between the different Veblen functions, let us call φF the Veblen function with finitely many variables, and φT the Veblen function with transfinitely many variables.
φF is a function which, when applied to a list of countable ordinals, gives a countable ordinal. A list of countable ordinals can be seen as a function which, when applied to a natural number, gives a countable ordinal, with the restriction that the result differs from 0 for finitely many integers. If we denote ω the set of natural numbers and Ω the set of countable ordinals, then this can be written : φF:(ω→Ω)→Ω. If we replace α→β by β^α, we get Ω^Ω^ω, and if we apply ψ to it, we get ψ(Ω^Ω^ω), which is the small Veblen ordinal, the least ordinal that cannot be reached using φF.
For φT, the position of a variable is represented by a countable ordinal instead of a natural number, also with the restriction that finitely many variables differ from 0, so we have φT:(Ω→Ω)→Ω. If we replace α→β by β^α, we get Ω^Ω^Ω, and if we apply ψ to it, we get ψ(Ω^Ω^Ω), which is the large Veblen ordinal, the least ordinal that cannot be reached using
If we extrapolate this correspondence, we can define a generalization of the Veblen function whose limit would be ψ(Ω^Ω^Ω^Ω), and the "position" of a variable would be a function which gives a countable ordinal when applied to a countable ordinal, and so on, up to the Howard ordinal, which is the limit of ψ(Ω),ψ(Ω^Ω),ψ(Ω^Ω^Ω),...
Correspondence between basic notation systems and their collapsing extensions based on formula : least fixed point of f = f(W)
Basic notation	Formula	Limit	Extension	Correspondence with basic notation	Crossing beyond limit
Cantor	cantor(a,b)=b+w^a	least a = cantor(a,0) = w^a = epsilon_0	Taranovsky	C(a,b) = b+w^a iff C(a,b) >= a	C(W,0) = epsilon_0
Epsilon	epsilon_a	least a = epsilon_a = zeta_0	Madore's psi	psi(a) = epsilon_a for all a < zeta_0	psi(W) = zeta_0
Binary Veblen	phi_a(b) or phi(a,b)	least a = phi(a,0) = Gamma_0	theta	theta(a,b) = phi(a,b) below Gamma_0	theta(W,0) = Gamma_0

Correspondence between different notations for some of the most important ordinals
Name	limit of Veblen	Simmons	Madore's psi	theta	Taranovsky
Gamma_0	phi_a(b) or phi(a,b)	[1] [0] Next w	psi(W^W)	theta(W,0)	C(W^2,0)
Small Veblen	finitely many variables phi(a_n,...,a_0)		psi(W^W^w)	theta(W^w,0)	C(W^w,0)
Large Veblen	transfinitely many variables phi	[2] [1] [0] Next w	psi(W^W^W)	theta(W^W,0)	C(W^W,0)
Bachmann Howard	extension of phi : T = T -> W phi(a1:...:an,b1:...:bn,...)	limit of ... [3] [2] [1] [0] Next w	psi(epsilon_(W+1)) = limit of psi(W^W^...^W)	theta(epsilon_(W+1),0)	C(C(W_2,W),0)

Taranovsky

module Taranovsky where

 -- Natural numbers
 data Nat
  = ZeroN
  | SucN Nat

 -- Ordinals
 data Ord
  = Zero
  | Suc Ord
  | Lim (Nat -> Ord)
  | Ext (Ord -> Ord)

 -- Ordinals
 --data Xord
 -- = Cnt Ord
 -- | Ext (Ord -> Xord)

 -- Ordinal corresponding to a given natural
 ordOfNat ZeroN = Zero
 ordOfNat (SucN n) = Suc (ordOfNat n)

 -- omega
 w = Lim ordOfNat

 -- plus a b = b + a
 plus Zero b = b
 plus (Suc a) b = Suc (plus a b)
 plus (Lim s) b = Lim (\n -> plus (s n) b)
 plus (Ext f) b = Ext (\x -> plus (f x) b)

 lim0 s = Lim s

{-
 fpower l f Zero x = x
 fpower l f (Suc a) x = f (fpower l f a x)
 fpower l f (Lim s) x = l (\n -> fpower l f (s n) x)

 -- fix f z = least fixed point of f which is > z
 fix f z = fpower lim0 f w (Suc z) -- Lim (\n -> fpower0 f (ordOfNat n) (Suc z))
-}

 iter f ZeroN a = a
 iter f (SucN p) a = iter f p (f a)

 opLim f a = Lim (\n -> f n a)

 opItw f = opLim (iter f)

 -- cantor a b = a + w^b -> C(b,a)
 cantor a Zero = Suc a
 cantor a (Suc b) = opItw (\x -> cantor x b) a
 cantor a (Lim s) = Lim (\n -> cantor a (s n))
 -- cantor a (Ext f) = Ext (\x -> cantor a (f x))
 cantor a (Ext f) = opItw (\x -> cantor a (f x)) Zero
 -- cantor a (Ext f) = cantor a (opItw (\x -> f (cantor a x)) Zero)

or

- Taranovsky's C(b,a) = generalization of a + w^b
 tc Zero a = Suc a
 tc (Suc b) a = opItw (tc b) a
 tc (Lim s) a = Lim (\n -> tc (s n) a)
 -- tc (Ext f) a = Ext (\x -> tc (f x) a)
 tc (Ext f) a = opItw (\x -> tc (f x) a) Zero
 -- tc (Ext f) a = tc (opItw (\x -> f (tc x a)) Zero) a

Exemple :
C(W,0) = C(Ext I, 0) = H [C(*,0)] 0
 = lim 0, C(0,0)=0+w^0=1, C(1,0)=0+w^1=w, C(w,0)=0+w^w=w^w, …
 = epsilon₀

https://stepstowardinfinity.wordpress.com/2015/06/22/ordinal3/

It seems that the Ω1 in C function works very similar to the Ω in θ function. And they are also very similar to my EAN: Ω1 or Ω expands into “ω layers of” the C or θ where they are, and the results are the supremum of any finite layers of the C or θ where the Ω1 or Ω is.
The 1st system only handles ordinals up to the Bachmann-Howard ordinal. So we need 2nd system now. In 2nd system, Ω1 = C(Ω2,0), and the Bachmann-Howard ordinal is the supremum of all the C(C(Ω2,0),0), C(C(C(Ω2,0),C(Ω2,0)),0), C(C(C(C(Ω2,0),C(Ω2,0)),C(Ω2,0)),0), C(C(C(C(C(Ω2,0),C(Ω2,0)),C(Ω2,0)),C(Ω2,0)),0), etc. Thus the BHO equals .

W1 = C(W2,0) = w^W2
BHO = lim C(W1,0), C(C(W1,W1),0), …
= C (H [C(*,W1)] W1, 0)
H [C(*,W1)] W1 = H (C(*,W1)] 0 ? = C(W2,W1)
= C (Ext [C(*,W1)], W1) ?
= C (Ext (x → C(x,W1)), W1) ?
Ou plutôt :
= C (Ext I, W1) = C (Ext (x → x), W1)

BHO = C(W^...^W,0)

C(W,W) = W*2
C(C(W,W),W) = W²
C(C(C(W,W),W),W) = W^W
C(C(C(C(W,W),W),W),W) = W^W^W

C(0,W) = W+1
C(C(0,W),W) = W*w
C(C(C(0,W),W),W) = W^w
C(C(C(C(0,W),W),W),W) = W^W^w

W^...^W^w = W^...^W ?
W^...^W = H [C(.,W)] 0 = C (Ext I, W) = C (Ext I, Ext I)
ou remplacer Ext f par Ext f z
avec tc (Ext f z) a = opItw (\x → tc (f x) a) z
C (Ext I W, W) avec W = Ext I 0 → C (Ext I (Exi I 0), Ext I 0)

W^...^W = C (Ext I W, W) avec W = Ext I 0
C(W,W) = W*2
C(W,0) = H [C(*,0)] 0
 = lim 0, C(0,0)=0+w^0=1, C(1,0)=0+w^1=w, C(w,0)=0+w^w=w^w, …
 = w^...^w = epsilon₀ = phi(1,0)
C(W,W) = H [C(*,W)] 0
 = lim 0,
C(0,W) = W+1,
C(W+1,W) = H [C(W,*)] W = W+w^(W+1) = W+w^W*w = W+epsilon_0*w
= lim W, C(W,W), … ? (boucle infinie)

Countable and extended (uncountable) ordinals :

module Cord_and_ord where

 -- Natural numbers
 data Nat
  = ZeroN
  | SucN Nat

 -- Countable ordinals
 data Cord
  = ZeroC
  | SucC Cord
  | LimC (Nat -> Cord)

 -- Ordinals
 data Ord
  = Zero
  | Suc Ord
  | Lim (Nat -> Ord)
  | Ext (Ord -> Ord)

 ordOfCord ZeroC = Zero
 ordOfCord (SucC a) = Suc (ordOfCord a)
 ordOfCord (LimC s) = Lim (\n -> ordOfCord (s n))

 cordOfOrd Zero = ZeroC
 cordOfOrd (Suc a) = SucC (cordOfOrd a)
 cordOfOrd (Lim s) = LimC (\n -> cordOfOrd (s n))
 cordOfOrd (Ext f) = cordOfOrd (f Zero)

ordinaux dénombrables : 0 | Suc Ord | Lim (Nat → Ord)
ordinaux non dénombrables : 0 | Suc Ord | Lim (Nat → Ord) | Ext (Ord → Ord)
   0 | Suc Ord | LimC (Nat → Ord) | LimU (Ord → Ord)
généralisation : LimX ((Ord → Ord) → Ord) ...
suite fondamentale transfinie a[n] avec n ordinal
exemple Buchholz :
http://googology.wikia.com/wiki/List_of_systems_of_fundamental_sequences
If α=ψν1(β1)+ψν2(β2)+⋯+ψνk(βk) where k≥2 then cof(α)=cof(ψνk(βk)) and α[η]=ψν1(β1)+⋯+ψνk−1(βk−1)+(ψνk(βk)[η]),
1. If α=ψ0(0)=1, then cof(α)=1 and α[0]=0,
2. If α=ψν+1(0), then cof(α)=Ων+1 and α[η]=Ων+1[η]=η,
3. If α=ψν(0) and cof(ν)∈{ω}∪{Ωμ+1|μ≥0}, then cof(α)=cof(ν) and α[η]=ψν[η](0)=Ων[η],
4. If α=ψν(β+1) then cof(α)=ω and α[η]=ψν(β)⋅η (and note: ψν(0)=Ων),
5. If α=ψν(β) and cof(β)∈{ω}∪{Ωμ+1|μ<ν} then cof(α)=cof(β) and α[η]=ψν(β[η]),
6. If α=ψν(β) and cof(β)∈{Ωμ+1|μ≥ν} then cof(α)=ω and α[η]=ψν(β[γ[η]]) where
7. {γ[0]=Ωμ γ[η+1]=ψμ(β[γ[η]]).

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=600

Now let's add something new to ordinal collapse!
W(x)0 = {0,1,ω,Ω,f()}
f(x) = ωx
W(x) = least k not in W(x)n for natural n.
Wf(x) = g(), where g() iterates the fixed points of k() for the least function k() such that sup{a, k(a), k(k(a)),...} = W(x), where a < W(x) and k() is a normal function. If no such k() exists, g() is the least function greater than any function in W(x)n for all natural n.
W(x)n+1 = W(x)n ∪ {a+b,a*b,f(a): a,b,f() in W(x)n} ∪ {W(y), Wf(y): y<x, y in W(x)n}
The big thing here is that we are now not just describing numbers, but including functions which can also describe those numbers.
What does that give us?
Well... at W(1) we gain the epsilon function. That means W(εΩ+1) is no longer our final stopping point. At W(2) we gain the zeta function, so W(ζΩ+1) is not our limit. W(Ω) gives us the gamma function. Where does it end? At W(εΩ+1+1) we get what you might as well call the Backhmann Howard function, for which BH0 = W(εΩ+1). That means we can have W(BHΩ+1) or what in other forms of collapse would require [imath]ψ(ε_{Ω_{1}+1})[/imath] to describe. But since we get that, we also get the function to describe it! That means we can call it on Ω+1 and get the equivalent of [imath]ψ(ε_{Ω_{2}+1})[/imath]. The fun stops at the equivalent of ψ(Ωω).
Since we've already had variants of this function, we already know the next step:
W(x)0 = {0,1,ω,Ω0,Ω1,f()}
Now we have W(Ω1) = ψ(Ωω).
So what is W(Ω12)?
Well, at W(Ω1) we got the function for which the first value is ψ(Ωω). Let's call that function L0() for now. So L0(0) = ψ(Ωω), and W(L0(Ω+1)) = ψ(Ωω). With that, W(Ω1+1) = ψ(ΩωΩ0), W(Ω1+2) = ψ(ΩωΩ02), and so on. This means W(Ω1+L0(Ω0+1)) =ψ(Ωω2) and [imath]W(Ω_{1}+ζ_{L_{0}(Ω_{0}+1)})[/imath] = ψ(Ωω+1). I'm fairly sure that means [imath]W(Ω_{1}+BH_{L_{0}(Ω_{0}+1)})[/imath] = [imath]ψ(ε_{Ω_{ω+1}})[/imath]. If so, then eventually we will have:
[imath]W(Ω_{1}+L_{0}(L_{0}(Ω_{0}+1)))[/imath] = [imath]ψ(ε_{Ω_{ω2}})[/imath]. If L1() is the fixed points of L0() then [imath]W(Ω_{1}+L_{1}(Ω_{0}+1))[/imath] = [imath]ψ(ε_{Ω_{ω^{2}}})[/imath], [imath]W(Ω_{1}+L_{2}(Ω_{0}+1))[/imath] = [imath]ψ(ε_{Ω_{ω^{3}}})[/imath], and so on; with La() giving us access to [imath]ψ(ε_{Ω_{ω^{1+a}}})[/imath]. W() incorporates L1() at W(Ω1+1) and L2() at W(Ω1+2).
Now, if I've got this all right, then W(Ω12) should be equal to ψ(a) for the least a such that a=Ωa.
But to be honest, I'm not totally sure, this stuff is a bit difficult to work with.
Last edited by WarDaft on Mon Nov 23, 2009 10:28 am UTC, edited 5 times in total.
All Shadow priest spells that deal Fire damage now appear green.
Big freaky cereal boxes of death.

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=640
Every ordinal less than the Large Veblen Ordinal can be found at some value of [imath]ψ(Ω^{Ω^{a}b+Ω^{c}d+..+Ωn}k+Ω^{Ω^{r}s+..+Ωx}y+..+z)[/imath], and the Large Veblen Ordinal itself becomes usable at [imath]ψ(Ω^{Ω^{Ω}})[/imath].
Beyond the Veblen hierarchy, there aren't any other simple systems to compare ordinal collapse to, but we can extend one to cover the function described above. If we let "/" imply a second line in the Veblen function, which denotes using the fixed points of the previous line, we can reach ψ(εΩ+1). We have φ(0/1) = [imath]ψ(Ω^{Ω^{Ω}})[/imath]. φ(n/1) denoting the nth limit of the f(a) = φ(1(a)): f(0), f(f(0)), f(f(f(0))),... sequence. φ(a,b,c,.../1) is extended the same way the initial veblen function is, save it is starting from φ(0/1) rather than φ(0,0). If we let φ(1(n)/1) denote a 1 in the nth position of the first line with a 1 in the second line, then the limit of f(a) = φ(1(a)/1): f(0), f(f(0)), f(f(f(0))),... can be considered φ(0/2). We extend the second line the same way we extended the first φ(0/a,b,c,...), leading us to φ(0/1(n)), a 1 in the nth term of the second line. The limit of f(a) = φ(0/1(a)) can then be considered φ(0/0/1). These lines again function as before. We can then consider the sequence φ(0/1), φ(0/0/1), φ(0/0/0/1), φ(0/0/0/0/1),... and the limit of this sequence as the number of lines reach ω is ψ(εΩ+1).
http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=680

Top
Allow me to redefine the brackets optimally.
[x] = [imath]ω \uparrow^x ω[/imath]
[ω, 1] = the limit of "[ω], [[ω]], [[[ω]]], [[[[ω]]]], [[[[[ω]]]]], ..."
[ω, a] = the limit of "[ω, a-1], [[ω, a-1], a-1], [[[ω, a-1], a-1], a-1], ..."
[ω, 0, 0] = the limit of "[0, ω], [0, [0, ω]], [0, [0, [0, ω]]], ..."
[ω, 1, 0] = the limit of "[ω, 0, 0], [[ω, 0, 0], 0, 0], [[[ω, 0, 0], 0, 0], 0, 0], ..."
[ω, a, 0] = the limit of "[ω, a-1, 0], [[ω, a-1, 0], a-1, 0], [[[ω, a-1, 0], a-1, 0], a-1, 0], ..."
[0, 0, 1] = the limit of "[0, ω, 0], [0, [0, ω, 0], 0], [0, [0, [0, ω, 0], 0], 0], ..."
etc.
[ω]1 = the limit of "[ω], [0, ω], [0, 0, ω], [0, 0, 0, ω], ..."
[ω, 1]1 = the limit of "[ω]1, [[ω]1]1, [[[ω]1]1]1, [[[[ω]1]1]1]1, ..."
[ω, 2]1 = the limit of "[ω, 1]1, [[ω, 1]1, 1]1, [[[ω, 1]1, 1]1, 1]1, ..."
etc.
[ω]2 = the limit of "[ω]1, [0, ω]1, [0, 0, ω]1, [0, 0, 0, ω]1, ..."
[ω]ω = the limit of "[ω]1, [ω]2, [ω]3, ..."
fO(x)(n) = [imath]f_{[ω]_{[ω]_{..._{[ω]_ω}}}}(n)[/imath] with x layers of subscripts.
1.) Which of these is equal to the LVO?
2.) Which of these, if any, is equal to the Bachman-Howard Ordinal?
3.) What is the growth rate of fO(ω)(n)?
KrazyerKate wrote:While it's probably the strangest sounding advice I will ever give, we need to stay focused on Hardcore Pornography in order to be successful.

I have a Blog and I make Games. I also have a big multiplayer game in the works (coming soonish!).

I've heard of that, but it seems like it would just open up to someone writing "the largest finite number that is expressible on a chalkboard", and then someone writing "the largest finite number that is expressible on a chalkboard + 1", and then bad things happening.
I'm still working on developing a new system, but I guess I have a question:
If K(x) = ωx, and Kn(x) = Kn-1n(x),
is Kω(ω) equal to [ω] or [imath]ω \uparrow^ω ω[/imath]?
If so, is [imath]K_{ω^2}(ω)[/imath] = [ω]1?
I'd peg the LVO at about [imath]K_{ω2}(ω)[/imath]
Is this on the right track at all?
I know if I'm aiming to make a power tower of ω, the result is not larger than [imath]ω \uparrow\uparrow ω[/imath], so I'm not aiming for that anymore.
KrazyerKate wrote:While it's probably the strangest sounding advice I will ever give, we need to stay focused on Hardcore Pornography in order to be successful.

I have a Blog and I make Games. I also have a big multiplayer game in the works (coming soonish!).

WarDaft
Posts: 1583
Joined: Thu Jul 30, 2009 3:16 pm UTC
### Re: My number is bigger!

Postby WarDaft » Mon Mar 01, 2010 2:37 am UTC
[ω,1]1 is the LVO.
Note that you have now essentially matched the extended veblen hierarchy with [], aside from using subtraction (which isn't so great), and using multiples of ω instead of 1 to count limits (which has virtually no impact on it at all actually).
[imath]f_{O(ω)}(n)[/imath] is equal to the collapse of the Bachmann Howard ordinal. Going much further in this method will prove very difficult and frustrating, trust me on that!
So in other words, [imath]f_{O(ω)}(n)[/imath] ~ y[ω(εC(0)+1)n]
Note that this is roughly the amount of recursive definition it would require to reach [imath]f_{ε_{0}}(n)[/imath] using strictly finite recursive functions

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=720
(p 19)
Λ() is a function that acts very similar to the Veblen function φ(), except instead of enumerating limits like ε0 and ζ0, it enumerates limits for uncountable ordinals.
Just like how φ(1,0) is the limit of "[imath]ω, ω^ω, ω^{ω^ω}, ω^{ω^{ω^ω}}, \cdots[/imath]", and φ(2,0) is the limit of "φ(1,0), φ(1,φ(1,0)), φ(1,φ(1,φ(1,0))), φ(1,φ(1,φ(1,φ(1,0)))), ..." (which is the same as the limit of "[imath]ε_0, ε_{ε_0}, ε_{ε_{ε_0}}, ε_{ε_{ε_{ε_0}}}, \cdots[/imath] or ζ0)"
Λ(1,0) is the limit of "[imath]ω, ω_ω, ω_{ω_ω}, ω_{ω_{ω_ω}}, \cdots[/imath]" and Λ(2,0) is the limit of "Λ(1,0), Λ(1,Λ(1,0)), Λ(1,Λ(1,Λ(1,0))), Λ(1,Λ(1,Λ(1,Λ(1,0)))), ..."
But of course, just like the Veblen functions, the real fun comes in the transfinite terms.
Λ(1@ω) is the limit of "Λ(1,0), Λ(1,0,0), Λ(1,0,0,0), Λ(1,0,0,0,0,0), ..."
But now I'm going to expand it to include a Λ1(1,0) which is the limit of "Λ(1,0), Λ(1@Λ(1,0)), Λ(1@Λ(1@Λ(1,0))), Λ(1@Λ(1@Λ(1@Λ(1,0)))), ..."
and then Λ1(2,0) would be the limit of "Λ1(1,0), Λ1(1,Λ1(1,0)), Λ1(1,Λ1(1,Λ1(1,0))), Λ1(1,Λ1(1,Λ1(1,Λ1(1,0)))), ..."
and then that Λ1() would also have transfinitely many entries enumerated by a Λ2() that is the limit of "Λ1(1,0), Λ1(1@Λ1(1,0)), Λ1(1@Λ1(1@Λ1(1,0))), Λ1(1@Λ1(1@Λ1(1@Λ1(1,0)))), ..."
(Note that the function Λ1() is not to be confused with the ordinal Λ1, which would be notated as Λ(1,1) in the Λ() functions.)
But wait! There's more!
Λω(1,0) is the limit of "Λ(1,0), Λ1(1,0), Λ2(1,0), Λ3(1,0), Λ4(1,0), ..."
and then there's also stuff like Λω(1,0,0), Λω+1(1,0), Λω2(1,0), [imath]Λ_{\Gamma_ω}(1,0)[/imath], ...
and then I define the ordinal ℘ to be the limit of "[imath]Λ(1,0), Λ_{Λ(1,0)}(1,0), Λ_{Λ_{Λ(1,0)}(1,0)}(1,0), Λ_{Λ_{Λ_{Λ(1,0)}(1,0)}(1,0)}(1,0), \cdots[/imath]".
and lastly, I define θ(α) to be the collapse of α.
and I enter the number fθ(℘)(4209).
Does that work?

M(n) is a set containing 0, 1, and every ωα from ω0 to ω1+n.
and C(n, 0, 0) = M(n)
and C(n, k, s+1) = C(n, k, s) ∪ {a+b, ab, ab, L(c, d) : a, b, c<n, k<d ∈ C(n, k, s)}
and L(c, d) is the smallest ordinal not in C(c, d, s) for any natural s.
and X(z) is the smallest ordinal that will not be in C(z, k, s) for any k or any natural s.
Then:
[imath]L(0, ω_1^{ω_1}) = \Gamma_1[/imath]
[imath]L(0, ω_1^{{ω_1}^{ω_1}})[/imath] is the Large Veblen Ordinal
[imath]X(0) = L(0, ε_{ω_1+1})[/imath], which is the Bachman Howard Ordinal
[imath]X(ω) = L(ω, ε_{ω_1+1})[/imath] I think is the Takeuti-Feferman-Buchholz ordinal, or [imath]ψ(ε_{ω_ω+1})[/imath].
...except that it should work with X(ω+1) and larger ordinals -- or at least I see no reason why it shouldn't.
And assuming that it does, couldn't we look for things like X(ω2), X(ωω), and X(ε0)? Would we able to find an X(ω1)?
Would X(X(X(ω))) have any merit? Xω(ω)? [imath]X^{ε_0}(ω)[/imath]?
If Λ0 was the smallest a such that a = ωa, would X(Λ0) be anything?
How large would [imath]f_{X(Λ_0)}(4209)[/imath] be?
Or [imath]f_{X(ω)}(4209)[/imath] for that matter?

Well, I messed that up -- but it's part of the learning process.
My next attempt is far more aggressive:
I'm defining a series of ordinals that go like this:
ж(0) is an ordinal larger than anything you can define with ω. It's larger than ω, larger than ωω, larger than ωω, larger than Λ(0,0), larger than Λ(1@ω), larger than ℘. ж(1) is larger than all of that including ordinals defined using ж(0) as well.
ж(α) will be larger than any ordinal not defined with ж(α). No amount of ordinal arithmetic, subscripting or fixed point functions on ж(α) that don't make use of ж(α+1) or something larger will ever be larger than ж(α+1).
ж(1,0) will be larger than any amount of ж(ж(ж(ж(...(α)))...). There is no β or α less than ж(1,0) that will make жβ(α) = ж(1,0).
ж(1,α+1) would then be larger than any amount of ordinal arithmetic, subscripting or fixed point functions on ж(1,α) that don't make use of ж(1,α+1) or anything larger.
ж(α+1,0) would then be larger than any ж(ж(ж(ж(...(α,0),0),0)...),0) for any length less than ж(α+1,0).
ж(1,0,0) would be larger than any ж(ж(ж(...(a,0),0),0)...),0) for any length less than ж(1,0,0) and so on through, and past, ж(1@ж(0)).
ж(1#0) is an ordinal I define to be larger than ж(1@β) for any β less than ж(1#0).
ж(1#0,1) would then be larger than any amount of ordinal arithmetic, subscripting or fixed point functions, and this would continue as previously to values like ж(1#0,1,0) ж(1#0,1,0,0), ж(1#0,1@ж(1@ж(0))), etc.
ж(1#1) would be larger than ж(1#0,1@β) for any β less than ж(1#1).
I then define a function Q() such that:
Q(0, 0) = {0, 1, ω}
Q(k, s+1) = Q(k, s) ∪ {a+b, ab, ab, ж(a), ж(a@b), ж(a#b) : a, b ∈ Q(k, s)} ∪ {βa : β0, a ∈ Q(k, s)} ∪ {ю(c) : c<k ∈ Q(k, s)}
ю(c) is the smallest ordinal not in Q(c, n) for any natural n.
This would mean that Q(1, 0) would contain ε0, and since Q(1, 1) can subscript anything that can possibly have a subscript, Q(1,1) will contain [imath]ε_{ε_0}[/imath], and Q(2,0) will contain ζ0 instead of ε1.
Q(1, 0) would also contain Λ0, and Q(2, 0) would contain Λ(1,0).
My number is then fю(δ)(4209) where δ is the largest ordinal contained in Q(ж(ω#ω),4209).
My previous number would be smaller than fю(δ)(2) where δ is [imath]ж(0)^{ж(0)^{ж(0)}}[/imath].
Also, just an interesting fact for kicks -- Graham's Number is smaller than fω+3(3).
-
PS: I don't think that f3(10) is roughly equal to the Hardy "decay" of ω3 because:
Hardy Decay
Step 1: ω3 -> ω2
Step 2: ω2 -> ω2
Step 3: ω2 -> ω+3
Step 6: ω->6
Step 12: 0
f3(10) Decay
f3(10) = f210(10) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f2(10)))))))))) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f110(10)))))))))) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f1(f1(f1(f1(f1(f1(f1(f1(f1(f1(10)))))))))))))))))))) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f1(f1(f1(f1(f1(f1(f1(f1(f1(f010(10)))))))))))))))))))) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f1(f1(f1(f1(f1(f1(f1(f1(f1(f0(f0(f0(f0(f0(f0(f0(f0(f0(f0(10)))))))))))))))))))))))))))))) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f1(f1(f1(f1(f1(f1(f1(f1(f1(10^^10))))))))))))))))))))) = f2(f2(f2(f2(f2(f2(f2(f2(f2(f1(f1(f1(f1(f1(f1(f1(f1(f010^^10(10^^10))))))))))))))))))))) = …

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=800

I notice that several posters to this thread seem familiar with Conway's arrow notation,
so maybe someone here might know of a published source on locating "n-arrow chains"
in an iterated-function hierarchy (e.g., Wainer or Hardy) ...
Consider the following three kinds of "n-arrow chain":
qk(x) ::= x → x → ... x → x (with k arrows)
(fixed number of arrows, variable equal arguments)
Qk(x) ::= k → k → ... k → k (with x arrows)
(fixed equal arguments, variable number of arrows)
D(x) ::= x → x → ... x → x (with x arrows)
(= Qx(x) = qx(x), diagonalising on both the number of arrows and on the arguments)
I believe I can prove the following w.r.t. the Wainer hierachy of functions fα:
qk << fω(k-1)+3
Qk << fω2
where g << fα means that g(x) < fα(x) for all sufficiently large x.
But what is the least α for which
D << fα ?????
(It seems likely to me that α ≤ ωω, but I would really like to see a proof.)
Does anyone here know of sources for proofs of results along these lines?

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=840 p 22
Okay, let’s define a monstrously large recursive ordinal! (and a large finite
number)
When last we left, we defined a transfinite hierarchy over Q and theta,
indexed by a large ordinal xi. We want to define larger and larger powers of xi.
We will write Q(a)(b) and theta0 (a) instead of Qa(b) and thetaa. Also, replace
xi with theta1(0).
As before, we define an inaccessible hierarchy above xi, by I(1)(0)(a1@b1,
a2@b2, ... an@bn). We then define Q(1)(0) and theta0(1)(0) so that
Q(1)(0)(θ 0 (1)(0) a 1 b 1 +θ 0 (1)(0) a 2 b 2 +...θ 0 (1)(0) a n b n ) = I(1)(0)(b 1 @a 1 , b 2 @a 2 , ...b n @a n ).
We can then extend this by defining Q(1)(1) and theta0 (1)(1), Q(1)(alpha)
and theta 0(1)(alpha) for arbitrary ordinals alpha, and then a transfinite hier-
archy Q(1)(a1@b1, ... ,an@bn) and theta0(1)(a1@b1, ... ,an@bn). Next, we
define a new large ordinal theta1(1) (we can take this to be the second weakly
compact cardinal), to diagonlize over the transfinite hiearachy, and we define
Q(1)(θ 1 (1) a 1 b 1 +θ 1 (1) a 2 b 2 +...θ 1 (1) a n b n )(c) = Q(1)(b 1 @a 1 , b 2 @a 2 , ..., b n @a n )(c)
θ 0 (1)(θ 1 (1) a 1 b 1 + θ 1 (1) a 2 b 2 + ...θ 1 (1) a n b n ) = θ 0 (1)(b 1 @a 1 , b 2 @a 2 , ..., b n @a n ).
Continuing the entire procedure above, we can define Q(a)(b)(c), theta0(a)(b)
and theta1(a) for arbitrary ordinals a,b,c. Again, we can extend this to trans-
finite hierarchies Q(a1@b1, ... ,an@bn) (b)(c), theta0(a1@b1, ... ,an@bn) (b)
and theta1(a1@b1, ... ,an@bn). Now we define a large ordinal theta2(0) (let’s
take this to be the smallest 1-indescribable ordinal) to index these transfinite
hierarchies.
Q(θ 2 (0) a 1 b 1 +θ 2 (0) a 2 b 2 +...θ 2 (0) a n b n )(c)(d) = Q(b 1 @a 1 , b 2 @a 2 , ..., b n @a n )(c)(d)
θ 0 (θ 2 (0) a 1 b 1 +θ 2 (0) a 2 b 2 +...θ 2 (0) a n b n )(c) = θ 0 (b 1 @a 1 , b 2 @a 2 , ..., b n @a n )(c) θ 1 (θ 2 (0) a 1 b 1 +
θ 2 (0) a 2 b 2 + ...θ 2 (0) a n b n ) = θ 1 (b 1 @a 1 , b 2 @a 2 , ..., b n @a n )
So we can define our notation by
C 0 (α, β) = β ∪ {0, θ 2 (0)}
C n+1 (α, β) = {γ+δ, γδ, γ δ , φ(γ, δ), Q(γ, δ, #), θ 0 (γ, δ), θ 1 (γ)|γ, δ, # ∈ C n (α, β)}
∪C m (γ, δ|γ, δ, m ∈ C n (α, β), m < ω ∪{ψ γ (δ)|γ, δ ∈ C n (α, β), δ < α, γ a regular
cardinal} ∪{τ (γ,
S δ)|γ, δ ∈ C n (α, β), γ < α}
C(α, β) = C n (α, β)
ψ α (β) = min{γ : α ∈ C(β, γ) ∧ C(β, γ) ∩ α ⊆ γ}
τ (α, β) = the βth ordinal γ such that γ ∈
/ C(α, γ)
Okay, let’s keep going. theta2(0) can be extended by an inaccessible hiear-
achy Q(1)(0)(0)(a) and theta0(1)(0)(0). We proceed on, extending our notations
in the usual manner, defining Q(1)(a)(b)(c), theta0(1)(a)(b), and theta1(1)(a).
We extend the variable a into a transfinite hierarchy, e.g. Q(1)(a1@b1, ...
,an@bn)(c)(d), and then define theta2(1) (as the second smallest 1-indescribable
cardinal) to index our new transfinite heirarchy. So
Q(1)(θ 2 (1) a 1 b 1 +θ 2 (1) a 2 b 2 +...θ 2 (1) a n b n )(c)(d) = Q(1)(b 1 @a 1 , b 2 @a 2 , ..., b n @a n )(c)(d)
θ 0 (1)(θ 2 (1) a 1 b 1 +θ 2 (1) a 2 b 2 +...θ 2 (1) a n b n )(c) = θ 0 (1)(b 1 @a 1 , b 2 @a 2 , ..., b n @a n )(c)
θ 1 (1)(θ 2 (1) a 1 b 1 + θ 2 (1) a 2 b 2 + ...θ 2 (1) a n b n ) = θ 1 (1)(b 1 @a 1 , b 2 @a 2 , ..., b n @a n ).
This extends upwards for all ordinals, so that we have Q(a)(b)(c)(d), theta0(a)(b)(c),
theta1(a)(b), and theta2(a) defijned for all a. We extend to a transfinite hi-
erarchy again, and next define a large ordinal theta3(0) (call it the smallest
2-indescribable cardinal) to index over it.
1I think you can see how to proceed from here. We get longer and longer
functions with more and more parameters. Eventually we can define Q for
an arbitrary number of parameters, and define thetan for an arbitrary natural
number n and an arbitrary number of parameters.
For convenience, we represent Q(a1@b1)(a2@b2)...(an)(bn) to indicate an
a1 in the b1 place, an a2 in the b2 place, etc. We can then define
C 0 (α, β) = β ∪ {0}
C n+1 (α, β) = {γ+δ, γδ, γ δ , φ(γ, δ), Q(γ 1 @δ 1 )(γ 2 @δ 2 )...(γ m @δ m ), θ k (γ 1 @δ 1 )(γ 2 @δ 2 )...(γ m @δ m )|γ, δ, #, γ i ,
C n (α, β), δ i , m, k < ω} ∪C m (γ, δ|γ, δ, m ∈ C n (α, β), m < ω ∪{ψ γ (δ)|γ, δ ∈
C n (α, β), δ < α,
S γ a regular cardinal} ∪{τ (γ, δ)|γ, δ ∈ C n (α, β), γ < α}
C(α, β) = C n (α, β)
ψ α (β) = min{γ : α ∈ C(β, γ) ∧ C(β, γ) ∩ α ⊆ γ}
τ (α, β) = the βth ordinal γ such that γ ∈
/ C(α, γ)
Next, we want to define Q and theta for transfinite parameters. I’m having
a bit of trouble with this, so I’ll continue in a later post.
2

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=920 p 24

I was looking back and I realized I completely missed your June 30 post.
So here's a redefinition:
Define an ordinal creation function q[x]
q[0](3) = θ(3) = θ3
q[0](a@cb) = θ(a@cb)
q[1](a@cb) = λ(a@cb)
q[0](q[1]) = θ(λ) = θ(1@@1)
q[0](q[0](q[1])ba) = q[0](a@b) = θ(a@b)
~
Define a transfinite heirarchy of transfinite heirarchies in the form of I(a@cb)
I(a@0b) = I(a@b)
I(a@3b) = I(a@@@@b)
q[c] can be used to index I(a@cb)
Q(q[c]ba) = I(a@cb)
Q(q[3]ba + q[2]dc) = I(a@@@@b)(d@@@c)
~
Define the collapsing function:
C(k, l, 0) = {a : a<l} ∪ 0
C(k, l, s+1) = {a+b, ab, ab, φ(a,b), q[a](b), Q(a), C(a,b,c), ψ(d,e), τ(d,a) : a, b, c<ω, d<k, e is a regular cardinal ∈ C(k, l, s)}
C(k, l, ω) = { C(k, l, a) : a < ω }
φ(y, z) is the Veblen function.
ψ(y, z) = min{a : z ∈ C(y,a,ω), C(y,a,ω)∩z ⊆a}
τ(y, z) is the zth ordinal a such that a ∉ C(y,a,ω)
~
Define our arbitrarily large number: C(Q(q[Γ4]209), g4209, g4209)

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=1040

Here we go with the notation. It's a bit much to do in one go, so I will probably post it in parts and edit this post as I go.
Define a cardinal to be 0-weakly inaccessible if it is a regular limit cardinal.
(A cardinal alpha is regular if it is not the union of fewer than alpha many smaller ordinals;
a cardinal is limit if it is ωα for α limit.)
A cardinal is α+1-weakly inaccessible if it is an α-weakly inaccessible cardinal and a limit of α-weakly inaccessible cardinals.
A cardinal is β-weakly inaccessible for β limit if it is α-weakly inaccessible for all α < β.
A cardinal α is (1,0)-weakly inaccessible if it is α-weakly inaccessible.
A cardinal α is (2,0)-weakly inaccessible if it is (1,α)-weakly inaccessible.
A cardinal α is (α,0)-weakly inaccessible for α limit if it is (β,0)-weakly inaccessible for all β < α.
A cardinal α is (1,0,0)-weakly inaccessible if it is (α,0)-weakly inaccessible.
A cardinal α is (2,0,0)-weakly inaccessible if it is (1,α,0)-weakly inaccessible.
A cardinal α is (α,0,0)-weakly inaccessible for α limit if it is (β,0,0)-weakly inaccessible for all β < α.
and so on.
Denote (a@8,b@6,c@4,d@1) to mean (a,0,b,0,c,0,0,d), for instance. This notation allows us to go express transfinite places like (1@ω)
A cardinal is (1@ω)-weakly inaccessible if it is (1@n)-weakly inaccessible for all n < ω.
A cardinal is (2@ω)-weakly inaccessible if it is (1@ω,1@n)-weakly inaccessible for all n < ω.
A cardinal α is (α@ω)-weakly inaccessible for α limit if it is (β@ω)-weakly inaccessible for all β < α.
More generally,
A cardinal γ is (a1@b1, a2@b2,..., an+1@1[/sub])-weakly inaccessible if it is (a1@b1, a2@b2,..., an@1[/sub])-weakly inaccessible and a limit of (a1@b1, a2@b2,..., an+1@1[/sub])-weakly inaccessible cardinals.
A cardinal γ is (a1@b1, a2@b2,..., an+1@bn+1)-weakly inaccessible if it is (a1@b1, a2@b2,..., an@bn+1, γ@bn)-weakly inaccessible.
A cardinal γ is (a1@b1, a2@b2,..., an+1@bn)-weakly inaccessible (with b_n limit) if it is (a1@b1, a2@b2,..., an@bn, 1@c)-weakly inaccessible for all c < bn.
A cardinal γ is (a1@b1, a2@b2,..., an@bn)-weakly inaccessible (with a_n limit) if it is (a1@b1, a2@b2,..., c@bn)-weakly inaccessible for c < an.
Finally, we define I(a1@b1, a2@b2,..., an@bn,c@0) to be the c'th (a1@b1, a2@b2,..., an@bn)-weakly inaccessible cardinal.
Next, define M to be the least weakly Mahlo cardinal. Define a function J(c) by writing c as Ma1*b1 + Ma2*b2 + Man*bn with the ai's decreasing and bi < M for all i, and letting
J(Ma1*b1 + Ma2*b2 + Man*bn) = I(b1@a1,b2@a2,..., bn@an).
We can now define an ordinal notation using J and M:
C(a,b,0) = b U {0,M}
C(a,b,n+1) = {c+d, cd, φ(c,d), J(c), ψ(e,f), τ(e,a), m(e,g,h) | c,d,e,f,g,h ∈ C(a,b,n), e < a, f a regular cardinal, g,h < ω}
C(a,b) = Un ∈ N C(a,b,n)
ψ(y, z) = min{a : z ∈ C(y,a,ω), C(y,a,ω) ∩ z ⊆ a}
τ(y, z) is the zth ordinal a such that a ∉ C(y,a)
m(x, y, z) is the largest finite ordinal in C(x, y, z)
Next, define I(1)(a1@b1, a2@b2,..., an@bn,c@0) to be an inaccessible hierarchy above M - that is, define I(1)(c) to be the c'th weakly inaccessible above M, and continue up the hierarchy as before.
Define M(1) to be the second least weakly Mahlo cardinal, and define
J(1)(M(1)a1*b1 + M(1)a2*b2 + M(1)an*bn) = I(1)(b1@a1,b2@a2,..., bn@an).
Similarly, define I(2), I(3),..., M(2), M(3),..., J(2), J(3), ... . Define I(ω)(a1@b1, a2@b2,..., an@bn,c@0) to be an inaccessible hierarchy above M(n) for all finite ordinals n, define M(ω) to be the ω'th smallest weakly Mahlo cardinal, and define
J(ω)(M(ω)a1*b1 + M(ω)a2*b2 + M(ω)an*bn) = I(ω)(b1@a1,b2@a2,..., bn@an).
So we see how to extend to all ordinals.
Our second notation system is
C(a,b,0) = b U {0}
C(a,b,n+1) = {c+d, cd, φ(c,d), J(c)(d), M(c), ψ(e,f), τ(e,a), m(e,g,h) | c,d,e,f,g,h ∈ C(a,b,n), e < a, f a regular cardinal, g,h < ω}
C(a,b) = Un ∈ N C(a,b,n)
ψ(y, z) = min{a : z ∈ C(y,a,ω), C(y,a,ω) ∩ z ⊆ a}
τ(y, z) is the zth ordinal a such that a ∉ C(y,a)
m(x, y, z) is the largest finite ordinal in C(x, y, z)
Define I(1,0)(a1@b1, a2@b2,..., an@bn,c@0) to be an inaccessible hierarchy above the least hyper-weakly Mahlo cardinal. Define M(1,0) to be the smallest weakly Mahlo cardinal above the least hyper-weakly Mahlo cardinal, and define
J(1,0)(M(1,0)a1*b1 + M(1,0)a2*b2 + M(1,0)an*bn) = I(1,0)(b1@a1,b2@a2,..., bn@an).
Continue on defining I(1,a), M(1,a), J(1,a) for ordinals a. M(1,a) will be the (1+a)'th smallest weakly Mahlo cardinal above the smallest hyper-weakly Mahlo cardinal. I(2,0) (a1@b1, a2@b2,..., an@bn,c@0) will then be an inaccessible hierarchy above the second smallest hyper-weakly Mahlo cardinal, and M(2,0) will be the smallest weakly Mahlo cardinal above that. The process continues throughout the ordinals.
Next, we define I(1,0,0)(a1@b1, a2@b2,..., an@bn,c@0) to be an inaccessible hierarchy above the smallest hyper-hyper-weakly Mahlo cardinal (or 2-weakly Mahlo cardinal). M(1,0,0) will be the next weakly Mahlo cardinal above that, and
J(1,0,0)(M(1,0,0)a1*b1 + M(1,0,0)a2*b2 + M(1,0,0)an*bn) = I(1,0,0)(b1@a1,b2@a2,..., bn@an).
We see how to continue this process for arbitrarily many places. I(1@ω) will be an inaccessible hierarchy above the smallest ω-weakly Mahlo cardinal, M(1@ω) will be the smallest weakly Mahlo cardinal above that, and J(1@ω) will be defined as usual.
We now have a transfinite hierarchy if I,M, and J; we will contract these hierarchies to exponential expressions over a larger cardinal. Define M(1)(0) to be the smallest (1,0)-weakly Mahlo cardinal, i.e. the smallest cardinal α such that α is α-weakly Mahlo. We will redefine J(c)(d) by expressing c as M(1)(0)a1*b1 + M(1)(0)a2*b2 ... + M(1)(0)an*bn, and defining
J(M(1)(0)a1*b1 + M(1)(0)a2*b2 ... + M(1)(0)an*bn)(d) = J(b1@a1, b2@a2, ..., bn@an)(d)
Similarly,
M(M(1)(0)a1*b1 + M(1)(0)a2*b2 ... + M(1)(0)an*bn) = M(b1@a1, b2@a2, ..., bn@an)
So we come to our third notation. (letting λ = M(1)(0) )
C(a,b,0) = b U {0, λ}
C(a,b,n+1) = {c+d, cd, φ(c,d), J(c)(d), M(c), ψ(e,f), τ(e,a), m(e,g,h) | c,d,e,f,g,h ∈ C(a,b,n), e < a, f a regular cardinal, g,h < ω}
C(a,b) = Un ∈ N C(a,b,n)
ψ(y, z) = min{a : z ∈ C(y,a,ω), C(y,a,ω) ∩ z ⊆ a}
τ(y, z) is the zth ordinal a such that a ∉ C(y,a)
m(x, y, z) is the largest finite ordinal in C(x, y, z)
We continue onward, building up a hierarchy J(1)(a1@b1,a2@b2, ... ,an@bn) M(1)(a1@b1,a2@b2, ... ,an@bn). We define M(2)(0) to be the second smallest (1,0)-weakly Mahlo cardinal, and define
J(1)(M(2)(0)a1*b1 + M(2)(0)a2*b2 ... + M(2)(0)an*bn)(d) = J(1)(b1@a1, b2@a2, ..., bn@an)(d)
We see how to extend J(a)(b)(c) and M(a)(b) to arbitrary ordinals a.
We next define a hierarchy J(1,0)(b)(c) and M(1,0)(b) above the smallest (1,1)-weakly Mahlo cardinal (a regular cardinal such that the (1,0)-weakly-Mahlo cardinals below it are stationary), and continue the process to J(a,b)(c)(d) and M(a,b)(c), J(a,b,c)(d)(e) and M(a,b,c)(d), and so on to arbitrary many places. We then define M(1)(0)(0) as the smallest (2,0)-weakly Mahlo cardinal (a cardinal alpha that is (1,alpha)-weakly Mahlo), and define
J(M(1)(0)(0)a1*b1 + M(1)(0)(0)a2*b2 ... + M(1)(0)(0)an*bn)(c)(d) = J(b1@a1, b2@a2, ..., bn@an)(c)(d)
Continuing in this fashion, we define J(a1)(a2)...(an)(b) and M(a1)(a2)...(an), and then J(a1@@b1)(a2@@b2)...(an@@bn)(c) and M(a1@@b1)(a2@@b2)...(an@@bn) (We use the @@ symbol to differentiate from the previous use of @ for lists within parentheses.). We define M((1))((0)) as the smallest (1,0,0)-weakly Mahlo cardinal (a cardinal alpha that is (alpha,0)-weakly Mahlo) and define
J(M((1))((0))a1*b1 + M((1))((0))a2*b2 ... + M((1))((0))an*bn)(c) = J(b1@@a1) (b2@@a2), ..., (bn@@an)(c)
So we arrive at our fourth notation, which is written identically to the previous notation, except that λ = M((1))((0)) and J and M have new definitions.
We continue the hierarchies as before, Generally speaking, say we have hierarchies J((d))((a1@b1)(a2@b2)...(an@bn))(c) and M((d))((a1@b1)(a2@b2)...(an@bn)), and define M((d+1))((0)) as the (d+1)st smallest (1,0,0)-weakly Mahlo cardinal. Define as before
J((d))(M((d+1))((0))a1*b1 + M((d+1))((0))a2*b2 ... + M((d+1))((0))an*bn)(c) = J((d))(b1@@a1) (b2@@a2), ..., (bn@@an)(c),
and continue in this fashion through all ordinals. We extend to J((1,0))((...))(c), and M((1,0))((...)), then J((a1@b1,a2@b2,...,an@bn))((...))(c) and M((a1@b1,a2@b2,...,an@bn))((...)), and eventually J((a1@@b1)(a2@@b2)...(an@@bn))((...))(c) and M((a1@@b1)(a2@@b2)...(an@@bn))((...)). We then define M((1))((0))((0)) as the smallest (2,0,0)-weakly Mahlo cardinal, and define
J((M((1))((0))((0))a1*b1 + M((1))((0))((0))a2*b2 ... + M((1))((0))((0))an*bn)((c))(d) = J(b1@@a1) (b2@@a2), ..., (bn@@an)((c))(d)
We can continue this to define J((a1@@@b1))((a2@@@b2))...((an@@@bn))(c) and M((a1@@@b1))((a2@@@b2))...((an@@@bn)) and define M(((1)))(((0))) to be the smallest (1,0,0,0)-weakly Mahlo cardinal (the smallest cardinal alpha such that alpha is (alpha,0,0)-weakly Mahlo). Then define
J((M(((1)))(((0)))a1*b1 + M(((1)))(((0)))a2*b2 ... + M(((1)))(((0)))an*bn)(d) = J((b1@@@a1)) ((b2@@@a2)) ... ((bn@@@an))(d).
Similarly, we can extend this to J(((a1@@@@b1)))(((a2@@@@b2)))...(((an@@@@bn)))(c) and M(((a1@@@@b1)))(((a2@@@@b2)))...(((an@@@@bn))), and define M((((1))))((((0)))), etc.
We thus can define up to arbitrary numbers of parentheses and @ symbols. To extend to the transfinite, we use @k to mean k many @'s, for possibly infinite k. A typical example under the new notation is J(A1,A2,...,An) where Ai is of the form a @b1 c1 @ b2 c2 ... @bm cm, with c1 < c2 < ... < cm.
We make one final extension. Letting λ be the smallest weakly compact cardinal, we associate to each A_i = a @b1 c1 @ b2 c2 ... @bm cm the ordinal
[imath]o(A_i) = \lambda^{\lambda^{b_m} c_m + \lambda^{b_{m-1}} c_{m-1} + ... + \lambda^{b_1} c_1} a[/imath]
and redefine J(o(A1) + o(A2 + ... o(An)) = J(A1,A2,...,An)
Our final notation is still
C(a,b,0) = b U {0, λ}
C(a,b,n+1) = {c+d, cd, φ(c,d), J(c)(d), M(c), ψ(e,f), τ(e,a), m(e,g,h) | c,d,e,f,g,h ∈ C(a,b,n), e < a, f a regular cardinal, g,h < ω}
C(a,b) = Un ∈ N C(a,b,n)
ψ(y, z) = min{a : z ∈ C(y,a,ω), C(y,a,ω) ∩ z ⊆ a}
τ(y, z) is the zth ordinal a such that a ∉ C(y,a)
m(x, y, z) is the largest finite ordinal in C(x, y, z)
and we choose as our large finite number m(λ,42,42).
Last edited by Deedlit on Fri Aug 19, 2011 7:22 am UTC, edited 3 times in total.

http://forums.xkcd.com/viewtopic.php?f=14&t=7469&start=1120

Hmm, it's easier to just say what he did than search through this gigantic thread.
Define F1(x) = x+1. For i >= 2, define Fi by
Fi fi-1 fi-2 ... f1(x) = fi-1x fi-2 ... f1(x)
for arbitrary functionals fj of type j, 1 <= j <= i-1. Itaibn takes his number to be
F67 F66 ... F1 (67).
I don't see how to extend to infinite types without having your numbers go infinite. However, you can extend to infinite types when we define functions on ordinals.
Harold Simmons in "A comparison of two systems of ordinal notations" defines the following construction for functionals on ordinals:
Let Fix be the type 2 functional defined by
Fix f (x) = fomega(x+1) (i.e. the limit as n goes to infinity of fn (x+1) )
Letting o(x) = omegax, define
Next (x) = Fix o (x)
For arbitrary functionals fi of type i with 1 <= i <= n+1, define
g(x) = fn+1x fn ... f1 (0)
and define [n] as an n+2 type functional by
[n] fn+1 fn ... f1 (x) = Fix g (x).
Then the limit as n goes to infinity of [n] [n-1] ... [0] Next (0) is the Bachmann-Howard ordinal.
---------------------------------
Extending to infinite types is tricky - we can define a functional of type alpha as a function from the product of functionals of all types < alpha to ordinals. The problem is, if we are to extend Simmons' construction, is how are we going to define the functionals at limit ordinals? I'll have to think about it.

w^a = [suc→H,0→suc] a 0
epsilon₀ = R1 H suc 0 = H <H> I suc 0
w^epsilon₀ = R1 H H suc 0 = R1 H suc 0
point fixe suivant :
lim epsilon₀+1, w^(epsilon_0+1), w^w^(epsilon_0+1), …
w^(epsilon₀+1) = w^epsilon₀ * w = epsilon₀ * w
 = [suc→H,0→suc] (suc (R1 H suc 0)) 0 = H (R1 H H suc) 0 = H (R1 H suc) 0
w^w^(epsilon_0+1) = epsilon₀^w
 = H (R1 H H) suc 0 = H (R1 H) suc 0
w^w^w^(epsilon_0+1)
 = H (R1 H) H suc 0
w^w^w^(epsilon_0+1)
 = H (R1 H) H H suc 0
epsilon₁ = w^...^w^(epsilon_0+1) = H <H> (H (R1 H)) suc 0 = H <H> (H (H <H> I)) suc 0

epsilon₀ = R1 H suc 0
epsilon₀ * 2 = R1 H suc (R1 H suc 0)
epsilon₀ * w = H (R1 H suc) 0
epsilon₀ ² = R1 H (R1 H suc) 0
epsilon₀ ^ w = H (R1 H) suc 0
epsilon₀ ^ epsilon₀ = R1 H (R1 H) suc 0
epsilon1 = epsilon0 ^ … ^ epsilon₀ = R1 (R1 H) suc 0 = H <H <H> I> suc 0

fonction	plus petit point fixe
a → 1+a	w
a → w+A	w²
a → w+A	w^w
a → w^a	epsilon₀
a→epsilon_a=phi(1,a)	zeta₀ = phi(2,0)
a→zeta_a=phi(2,a)	eta₀ = phi(3,0)
a → phi(b,a)	phi(b+1,0)
a → phi(a,0)	phi(1,0,0)

Phi f = énumération points fixes de f
Phi [1+*] = [w+*]
Phi [w+*] = [w² + *] = Phi² [1 + *]
Phi [w.*] = [w^w.(1+*)]
Phi [w^*] = [epsilon_*]
Phi [phi(a,*)] = [Phi(a+1,*)]
Phi [phi(*,0)] = [phi(1,0,*)]

Simmons
Fix f z = f^w (z+1) = H f (suc z)
Next = Fix [w^*]
Next 0 = epsilon₀
Next^(1+a) 0 = epsilon_a
[0] h = Fix [h^* 0]
[0] Next 0 = Fix [Next^* 0] 0
= lim
1
Next 0 = epsilon₀
Next^epsilon₀ 0 = epsilon_epsilon₀
…
= epsilon_..._epsilon₀
= zeta₀
[0]² Next 0 = [0] ([0] Next) 0 = Fix ([0] Next)^* 0] 0
= lim
1
[0] Next 0 = zeta₀
([0] Next)^zeta₀ 0 = zeta_zeta₀
= zeta_..._zeta₀ = eta₀ = phi(3,0)
[0]^a Next 0 = phi(1+a,0)
[1] [0] Next 0 = Fix [[0]^* Next 0] 0
= lim
1 = phi(0,0)
[0] Next 0 = zeta₀ = phi(2,0)
[0]^zeta₀ Next 0 = phi(phi(2,0),0)
… = phi(phi(phi(2,0),0),0)
= phi(1,0,0)
[2] [1] [0] Next 0 = Fix [[1]^* [0] Next 0] 0 = LVO ?
= lim
1
[1] [0] Next 0 = phi(1,0,0) = Gamma₀
[1]^Gamma₀ [0] Next 0
[1]⁰ [0] Next 0 = [0] Next 0 = zeta₀ = phi(2,0)
[1]¹ [0] Next 0 = [1] [0] Next 0 = Gamma₀ = phi(1,0,0)
[1]² [0] Next 0 = [1] ([1] [0]) Next 0 = Fix [([1] [0])^* Next 0] 0 = SVO ?
= lim
1
[1] [0] Next 0 = Gamma₀ = phi(1,0,0)
([1] [0])^Gamma₀ Next 0
([1] [0])^a Next 0 = ?
([1] [0])⁰ Next 0 = Next 0 = epsilon₀ = phi(1,0)
([1] [0])¹ Next 0 = [1] [0] Next 0 = zeta₀ = phi(2,0)
([1] [0])² Next 0 = [1] [0] ([1] [0] Next) 0 = Fix [[0]^* ([1] [0] Next) 0] 0 = phi(1,2,0)
([1] [0])^(1+a) Next 0 = phi(a,2,0) ?
= lim
1
[0] ([1] [0] Next) 0 = Fix [([1] [0] Next)^* 0] 0
= lim
1
[1] [0] Next 0 = Gamma₀ = phi(1,0,0)
([1] [0] Next)^Gamma₀ 0 = phi(1,0,Gamma₀)
phi(1,0,phi(1,0,Gamma₀))
…
= phi(1,1,0)
[0]^phi(1,1,0) ([1] [0] Next) 0 = phi(1,1,phi(1,1,a))
= phi(1,2,0)
([1] [0])^Gamma₀ Next 0 = phi(phi(1,0,0),2,0) ?
= SVO ?

[0]^a ([1] [0] Next) 0 = ?
[0]⁰ ([1] [0] Next) 0 = [1] [0] Next 0 = Gamma₀ = phi(1,0,0)
[0]¹ ([1] [0] Next) 0 = [0] ([1] [0] Next) 0 = phi(1,1,0)
[0]² ([1] [0] Next) 0 = [0] ([0] ([1] [0] Next)) 0 = Fix [([0] ([1] [0] Next))^* 0] 0
= lim
1
[0] ([1] [0] Next) 0 = phi(1,1,0)
([0] ([1] [0] Next))^phi(1,1,0) 0
([0] ([1] [0] Next))^a 0 = ?
([0] ([1] [0] Next))⁰ 0 = 0
[0] ([1] [0] Next) 0 = phi(1,1,0)
[0] ([1] [0] Next) ([0] ([1] [0] Next) 0) = [0] ([1] [0] Next) phi(1,1,0)
= point fixe suivant = phi(1,1,1)
[0]^(1+a) ([1] [0] Next) 0 = phi(1,1,a)

[0]^a f x = ?
[0]⁰ f 0 = f 0
[0]¹ f x0 = [0] f 0 = Fix [f^* 0] 0 = lim 1, f 0, f^(f 0) 0, …

([1] [0] Next)^a 0 = ? → ([1] [0] Next)^(1+a) 0 = phi(1,0,a)
([1] [0] Next)⁰ 0 = 0
([1] [0] Next)¹ 0 = [1] [0] Next 0 = Gamma₀ = phi(1,0,0)
([1] [0] Next)² 0 = [1] [0] Next ([1] [0] Next 0) = [1] [0] Next Gamma₀
= Fix [[0]* Next 0] Gamma₀
= lim
Gamma₀ + 1
[0]^(Gamma₀+1) Next 0 = phi(Gamma₀+1,0)
= deuxième point fixe de a → phi(a,0)
[1] [0] Next = Gamma suivant
([1] [0] Next)² 0 = phi(1,0,1)
([1] [0] Next)³ 0 = [1] [0] Next ([1] [0] Next ([1] [0] Next 0)) = [1] [0] Next phi(1,0,1)
= phi(1,0,2)
([1] [0] Next)^(1+a) 0 = phi(1,0,a)

Fix f z = f^w (z+1) = H f (suc z)
Next = Fix [w^*]
epsilon_a = phi(1,a) = Next^(1+a) 0
[0] h = Fix [h^* 0]
zeta₀ = phi(2,0) = least fixed point of [epsilon_*] = Fix [epsilon_*] 0 = Fix [Next^(1+*) 0] 0 = Fix [Next^* 0] 0 = [0] Next 0
Fix [Next^* 0] 0 = lim 1, Next 0 = epsilon₀, Next^epsilon₀ 0 =Next^(1+epsilon₀) 0 = epsilon_epsilon₀, … = epsilon_..._epsilon₀ = zeta₀
Fix [Next^(1+*) 0] 0 = lim 1, Next² 0 = Next (Next 0) = epsilon₁, … epsilon_..._epsilon₁ = zeta₀
zeta₁ = phi(2,1) = second fixed point of [epsilon_*] = Fix [epsilon_*] (zeta₀ + 1) = Fix [Next^(1+*) 0] ([0] Next 0) = Fix [Next^* 0] ([0] Next 0)
 = [0] Next ([0] Next 0)
zeta_a = phi(2,a) = ([0] Next)^(1+a) 0
eta₀ = phi(3,0) = least fixed point of [zeta_*] = Fix [zeta_*] 0 = Fix [([0] Next)^(1+*) 0] 0 = Fix [([0] Next)^* 0] 0 = [0] ([0] Next) 0 = [0]² Next 0
eta₁ = phi(3,1) = next fixed point = Fix [zeta_*] ([0]² Next 0) = Fix [([0] Next)^(1+*) 0] ([0]² Next 0) = Fix [([0] Next)^* 0] ([0]² Next 0)
 = [0] ([0] Next) ([0]² Next 0) = [0]² Next ([0]² Next 0) = ([0]² Next)² 0
eta_a = phi(3,a) = ([0]² Next)^(1+a) 0

phi(1,a) = Next^(1+a) 0
phi(2,a) = ([0] Next)^(1+a) 0
phi(3,a) = ([0]² Next)^(1+a) 0
phi(1+b,a) = ([0]^b Next)^(1+a) 0

Gamma₀ = phi(1,0,0) = least fixed point of [phi(*,0)] = least fixed point of [phi(1+*,0)]
 = Fix [phi(1+*,0)] 0
 = Fix [[0]^* Next 0] 0
 = [1] [0] Next 0
with [1] h g = Fix [h^* g 0]
phi(1,0,1) = next fixed point = Fix [[0]^* Next 0] ([1] [0] Next 0) = [1] [0] Next ([1] [0] Next 0) = ([1] [0] Next)² 0
phi(1,0,a) = ([1] [0] Next)^(1+a) 0
phi(1,1,0) = least fixed point of [phi(1,0,*)] = Fix [phi(1,0,*)] 0 = Fix [([1] [0] Next)^(1+*) 0] 0 = Fix [([1] [0] Next)^* 0] 0 = [0] ([1] [0] Next) 0
phi(1,1,1) = next fixed point = Fix [([1] [0] Next)^* 0] ([0] ([1] [0] Next) 0) = [0] ([1] [0] Next) ([0] ([1] [0] Next) 0) = ([0] ([1] [0] Next))² 0
phi(1,1,a) = ([0] ([1] [0] Next))^(1+a) 0
phi(1,2,0) = least fixed point of [phi(1,1,*)] = Fix [([0] ([1] [0] Next))^(1+*) 0] 0 = Fix [([0] ([1] [0] Next))^* 0] 0 = [0] ([0] ([1] [0] Next)) 0
 = [0]² ([1] [0] Next) 0
phi(1,2,1) = next fixed point ...
phi(1,2,a) = ([0]² ([1] [0] Next))^(1+a) 0

phi(1,0,a) = ([1] [0] Next)^(1+a) 0
phi(1,1,a) = ([0] ([1] [0] Next))^(1+a) 0
phi(1,2,a) = ([0]² ([1] [0] Next))^(1+a) 0
phi(1,b,a) = ([0]^b ([1] [0] Next))^(1+a) 0

phi(2,0,0) = least fixed point of [phi(1,*,0)] = Fix [phi(1,*,0)] 0 = Fix [[0]^* ([1] [0] Next) 0] 0 = [1] [0] ([1] [0] Next) 0) = ([1] [0])² Next 0
phi(2,0,a) = (([1] [0])² Next)^(1+a) 0
phi(2,1,0) = least fixed point of [phi(2,1,*)] = Fix [phi(2,1,*)] 0 = Fix [(([1] [0])² Next)^* 0] 0 = [0] (([1] [0])² Next) 0
phi(2,1,a) = ([0] (([1] [0])² Next))^(1+a) 0
phi(2,b,a) = ([0]^b (([1] [0])² Next))^(1+a) 0
phi(c,b,a) = ([0]^b (([1] [0])^c Next))^(1+a) 0

phi(1,0,0,0) = least fixed point of [phi(*,0,0)] = Fix [phi(*,0,0)] 0 = Fix [([1] [0])^* Next 0] 0 = [1] ([1] [0]) Next 0 = [1]² [0] Next 0
phi(1,0,0,a) = ([1]² [0] Next)^(1+a) 0
phi(1,0,1,0) = Fix [([1]² [0] Next)^* 0] 0 = [0] ([1]² [0]) 0
phi (1,0,1,a) = ([0] ([1]² [0] Next))^(1+a) 0
phi(1,0,b,a) = ([0]^b ([1]² [0] Next))^(1+a) 0
phi(1,1,0,0) = Fix [phi(1,0,*,0)] 0 = Fix [[0]^* ([1]² [0] Next) 0] 0 = [1] [0] ([1]² [0] Next) 0
phi(1,1,0,a) = ([1] [0] ([1]² [0] Next))^(1+a) 0
phi(1,1,1,0) = Fix [phi(1,1,0,*)] 0 = Fix [([1] [0] ([1]² [0] Next))^* 0] 0 = [0] ([1] [0] ([1]² [0] Next)) 0
phi(1,1,1,a) = ([0] ([1] [0] ([1]² [0] next)))^(1+a) 0
phi(1,1,b,a) = ([0]^b ([1] [0] ([1]² [0] Next)))^(1+a) 0
phi(1,2,0,0) = Fix [phi(1,1,*,0)] 0 = Fix [[0]^* ([1] [0] ([1]² [0] next)) 0] 0 = [1] [0] ([1] [0] ([1]² [0] Next)) 0 = ([1] [0])² ([1]² [0] Next) 0

phi(1,0,0,0) = [1]² [0] Next 0
phi(1,1,0,0) = [1] [0] ([1]² [0] Next) 0
phi(1,2,0,0) = ([1] [0])² ([1]² [0] Next) 0
phi(1,c,0,0) = ([1] [0])^c ([1]² [0] Next) 0
phi(1,c,b,a) = ([0]^b (([1] [0])^c ([1]² [0] Next)))^(1+a) 0
phi(2,0,0,0) = Fix [phi(1,*,0,0)] 0 = Fix [([1] [0])^* ([1]² [0] Next) 0] 0 = [1] ([1] [0]) ([1]² [0] Next) 0 = [1]² [0] ([1]² [0] Next) 0 = ([1]² [0])² Next 0
phi(d,0,0,0) = ([1]² [0])^d Next 0
phi(d,c,b,a) = ([0]^b (([1] [0])^c (([1]² [0])^d Next)))^(1+a) 0 = (([1]⁰ [0])^b (([1]¹ [0])^c (([1]² [0])^d Next)))^(1+a) 0

phi(1,0) = Next 0
phi(1,0,0) = [1] [0] Next 0
phi(1,0,0,0) = [1]² [0] Next 0
…
SVO = [1]^w [0] Next 0
LVO = [2] [1] [0] Next 0 = [2...0] Next 0
BHO = [w...0] Next 0
[1] [w..0] Next 0 = [w+1...0] Next 0
Fix [[*...0] Next 0] 0

Fix f = f^w (z+1) = H f (suc z)
N = Fix suc
[0] h = Fix [h^* 0]
[1] h g = Fix [h^* g 0]
…
… [3] [2] [1] [0] N 0 ?
[0] N 0 = Fix [N^* 0] 0 = lim 1, N¹ 0 = w, N^w 0 = w.w = w², N^w² 0 = w.w² = w³, … = w^w
[0]² N 0 = [0] ([0] N) 0 = Fix [([0] N)^* 0] 0
 = lim
1
[0] N 0 = w^w
([0] N)^w^w 0 = w^w . w^w = (w^w)² = w^(w.2)
([0] N)² 0 = [0] N ([0] N 0) = w^w . 2
[0] N a = Fix [N^* 0] a = lim a+1, a+1+w = a+w, a+w², … = a+w^w
([0] N)^a 0 = w^w . a
 = w^w²
[0]^a N 0 = w^w^a
[1] h g = Fix [h^* g 0]
[1] [0] N a = Fix [[0]^* N 0] a
 = lim
a+1
[0]^(a+1) N 0 = w^w^(a+1)
[0]^(w^w^(a+1)) N 0 = w^w^w^w^(a+1)
 = Next a
[1] [0] N = Next

([0]^b ([1] [0] N))^(1+a) = phi(1+b,a)

https://core.ac.uk/download/pdf/33091421.pdf
Veblen function and klammersymbols
page 25
We introduce now the concept of Klammersymbols
which are a generalization of the finitary Veblen functions to the transfinite by
allowing arguments to be indexed by ordinals and which were introduced
by K. Schütte in [Sch54].

page 27
phi(x) = phi1(x) = w^x
phi1 xn … x0 = phi1 ( x0 … xn )
        ( 0 … n )

LVO = min a : a = phi1 ( 1 ) = phi (a → 1)
        ( a )

SVO = phi1 ( 1 ) = phi ( w → 1 )
        ( w )

page 29
phi_(n+1)(a1,…,a_(n+1)) = phi_1(a_(n+1) a_n … a₁ )
        ( 0 1 … n )

Simmons
http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/FruitHelp.pdf
( z 1+a(1) … 1+a(s) ) f = ( ( Nabla [ a(1)+1 ] o [0] o … o Nabla [ a(s)+1 ] o [0]) (Fix f))⁽1+z) 0
( 0 1+i(1) … 1+i(s) ) [ i(1)+1 ] [ i(s)+1 ]

Nabla [ a+1 ] = ([1]^i [0])⁽1+a)
        [ i+1 ]
not quite right when i=1 and a finite

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/FromBelow.pdf
Nabla [ a+1 ] = { ([1]^i [0])^(1+a) if i!=0
        [ i+1 ] { [0]^a if i=0

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/LambdaH.pdf
S [ a+1 ] f z = (([1]^i [0])^(1+a) (Fix f))^(1+z) 0
   [ i+1 ]

f ( z 1+a(1) … 1+a(s) ) = ((S[a(1)+1] o … o S[a(s)+1] f) z
  ( r 1+i(1) … 1+i(s) ) [i(1)+1] [i(s)+1] r

phi(1+a,b) = ([0]^a Next)^(1+b) 0
= ( b 1+a ) [w^*] = ((Nabla[a+1] o [0]) Next)^(1+b) 0
    ( 0 1 ) [1]

= ((([1]⁰ [0])^(1+a) o [0]) Next)^(1+b) 0
= (([0]^(1+a) o [0]) Next)^(1+b) 0
= ( [0]^(2+a) Next)^(1+b) 0 ?

phi(1,0) = epsilon₀ = Next 0 = [0]⁰ Next 0
( 0 1 ) = ([1]⁰ [0])¹ ([0] Next) 0 = [0]² Next 0 ?
( 0 1 )

phi(a,b,c) = ([0]^b (([1] [0])^a Next))^(1+c) 0
phi(a,b,c,d) = ([0]^c (([1][0])^b (([1]² [0])^a Next)))^(1+d) 0
ou
phi(1+a,1+b ,1+c,d) = ([0]^c (([1][0])^b (([1]² [0])^a Next)))^(1+d) 0 ?

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/FromBelow.pdf
semble plus correct que les autres articles
p 32
Nabla [ a+1 ] = { ([1]^i [0])^(1+a) if i!=0
        [ i+1 ] { [0]^a if i=0
p 33
Nabla [ a+1 … b+1 ] = Nabla [ a+1 ] o [0] o … o [0] o Nabla [ b+1 ]
        [ i+1 … j+1 ] [ i+1 ] [ j+1 ]
sans o [0] à la fin
epsilon₀ = Next 0
phi(1+a,b) = ([0]^a Next)^(1+b) 0
= ( b 1+a ) [w^*] = ( Nabla [ a+1 ] Next)^(1+b) 0 = ([0]^a Next)^(1+b) 0
    ( 0 1 ) [ 1 ]
phi(a,b,c) = ([0]^b (([1] [0])^a Next))^(1+c) 0 si a>0
ou
phi(1+a,b,c) = ([0]^b (([1][0])^(1+a) Next))^(1+c) 0
phi(1+a,1+b,c) = ( c 1+b 1+a ) [w^*]
        ( 0 1 2 )
= ((Nabla [ b+1 ] o [0] o Nabla [ a+1 ]) Next)^(1+c) 0
= ([0]^b ([0] ([1] [0])^(1+a) Next))^(1+c) 0
= ([0]^(1+b) (([1] [0])^(1+a) Next))^(1+c) 0
aller-retour 1+a → a+1 → 1+a

phi(1+a,0,c) = (([1] [0])^(1+a) Next)^(1+c) 0
= ( c 1+a ) [w^*] = ( Nabla [ a+1 ] Next )^(1+c) 0
    ( 0 2 ) [ 2 ]
= (([1] [0])^(1+a) Next)^(1+c) 0

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/FromBelow.pdf : correct
3 aout 2009

http://www.cs.man.ac.uk/~hsimmons/DOCUMENTS/PAPERSandNOTES/FruitHelp.pdf :
9 février 2006
p18 :
faux : o [0] final
incomplet : Actually, this last definition is not quite right when i=0 and a is finite.

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/LambdaH.pdf
3 aout 2009
p 30 : pas clair … _r zeta ?

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/Fruitful.pdf : pas de Klammersymbol
3 aout 2009

http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf
16 nov 2006
p 23 :
faux : o [0] final

http://www.cs.man.ac.uk/~hsimmons/ORDINAL-NOTATIONS/IterTemplate.pdf
3 aout 2009
long
pas de Klammersymbol

Beyond LVO
Fix f z = f^w (z+1) = H f (suc z)
Next = Fix [w^*]
[0] h = Fix [h^* 0]
[1] h g = Fix [h^* g 0]
[2] h g f = Fix [h^* g f 0]
phi(1+a,b) = ([0]^a Next)^(1+b) 0
phi(a,b,c) = ([0]^b (([1] [0])^a Next))^(1+c) 0
LVO = lfp of [phi(*:1)] = Fix [[1]^* [0] Next 0] = [2] [1] [0] Next 0
1+a th fp = F(a) = phi'1(a) = ([2] [1] [0] Next)^(1+a) 0
lfp of F = G(0) = phi'2(0) = Fix [([2] [1] [0] Next)^* 0] 0 = [0] ([2] [1] [0] Next) 0
1+a th fp = G(a) = phi'2(a) = ([0] ([2] [1] [0] Next))^a 0
lfp of G = H(0) = phi'3(0) = Fix [(0] ([2] [1] [0] Next)))^* 0] 0 =[0] ([0] ([2] [1] [0] Next)) 0 = [0]² ([2] [1] [0] Next) 0
phi'_(1+a)(0) = [0]^a ([2] [1] [0] Next) 0
phi'_(1+a)(b) = phi'(1+a,b) = ([0]^a ([2] [1] [0] Next))^(1+b) 0
cf phi(1+a,b) = ([0]^a Next)^(1+b) 0
phi'(1,0,0) = lfp of [phi'(*,0)] = Fix [[0]^* ([2] [1] [0] Next) 0] 0 = [1] [0] ([2] [1] [0] Next) 0
cf phi(1,0,0) = [1] [0] Next 0
phi'(a,b,c) = ([0]^b (([1] [0])^a ([2] [1] [0] Next)))^(1+c) 0
LVO' = [2] [1] [0] ([2] [1] [0] Next) 0 = lfp of [[1]^* (0] ([2] [1] [0] Next) 0]
1+a th fp : ([2] [1] [0] ([2] [1] [0] Next))^(1+a) 0 = (([2] [1] [0])² Next)^(1+a) 0
Phi₀ = phi : Next
Phi₁ = phi' : [2] [1] [0] Next
Phi₂ = phi'' : ([2] [1] [0])² Next
lfp of a → Phi_a(1_a)

phi(1,0,0) = phi(2:1) = [1] [0] Next 0
phi(1,0,0,0) = phi(3,1) = [1]² [0] Next 0
phi(1+a:1) = [1]^a [0] Next 0
lfp : LVO = Fix [[1]^* [0] Next 0] 0 = [2] [1] [0] Next 0
phi = phi_[w^*]
phi_f(1+a:1) = [1]^a (0] (Fix f) 0
S f a = phi_f(1+a:1) = [1]^a [0] (Fix f) 0
S f = [[1]^* [0] (Fix f) 0]
example : S [w^*] = [[1]^* [0] Next 0]
Fix (S [w^*]) 0 = Fix [[1]^* [0] Next 0] 0 = [2] [1] [0] Next 0 = LVO
Fix (S [w^*]) a = [2] [1] [0] Next a
S (S [w^*]) = [[1]^* [0] (Fix (S [w^*])) 0] = [[1]^* [0] ([2] [1] [0] Next) 0]
lfp : ([2] [1] [0])² Next 0
S^a : ([2] [1] [0])^a Next
Fix [([2] [1] [0])^* Next 0] 0 = [1] ([2] [1] [0]) Next 0

LVO = [2] [1] [0] Next 0
([2] [1] [0])^a Next 0
fp Fix [([2] [1] [0])^* Next 0] 0 = [1] ([2] [1] [0]) Next 0
… [2] [1]([2] [1] [0]) Next 0
Fix [([2] [1])^* [0] Next 0] 0 = [2] ([2] [1]) [0] Next 0
[2]^a [1] [0] Next 0
Fix [[2]^* [1] [0] Next 0] 0 = [3] [2] [1] [0] Next 0

w^a = [suc→H, 0→suc] a 0

http://quibb.blogspot.fr/2012/03/infinity-countable-ordinals.html
epsilon₁ = sup { epsilon₀ , epsilon₀ ^ epsilon₀ , … }
epsilon_a' = sup { epsilon_a , epsilon_a ^epsilon_a , … }
epsilon_...epsilon₀ = zeta₀ ; epsilon_zeta₀ = zeta₀
epsilon_(zeta₀+1) = sup { zeta₀ , zeta₀ ^ zeta₀ , … }
zeta₁ = sup { zeta₀+1, epsilon_(zeta₀+1), … }
phi(0,0,1) = Gamma₀
phi(0,0,2) = Gamma₁ = sup { phi(0,0,1), phi(0,phi(0,0,1),1), … }

https://sites.google.com/site/largenumbers/home/4-2/fgh_c
epsilon₁ = lim { epsilon₀+1, w^(epsilon₀+1), … }

w^(epsilon₀+1) = w^epsilon₀ * w = epsilon₀ * w
w^w^(epsilon₀+1) = w^(epsilon₀ * w) = (w^epsilon₀)^w = epsilon₀^w
w^w^w^(epsilon₀+1) = w^epsilon₀^w
epsilon₀^epsilon₀^w = (w^epsilon₀)^epsilon₀^w = w^(epsilon₀*epsilon₀^w) = w^epsilon₀^w = w^w^w^(epsilon₀+1)

suc 0 = 1
H suc 0 = w
H suc (H suc 0) = w*2
H (H suc) 0 =w²
H H suc 0 = w^w
R₁ H suc 0 = w^...^w = epsilon₀ = phi(1,0)
R₁ H suc (R₁ H suc 0) = epsilon₀ * 2
R₁ H (R₁ H suc) 0 = epsilon₀²
R₁ H (R₁ H) suc 0 = epsilon₀ ^ epsilon₀
R₁ (R₁ H) suc 0 = epsilon₀ ^ … ^ epsilon₀ = epsilon₁
H R₁ H suc 0 = epsilon_w
R₁ H R₁ H suc 0 = epsilon_epsilon₀
R₂ R₁ H suc 0 = epsilon_..._epsilon₀ = zeta₀ = phi(2,0)
R₂ R₁ H (R₂ R₁ H) suc 0 = zeta₀ ^ zeta₀
R₁ (R₂ R₁ H) suc 0 = zeta₀ ^ … ^ zeta₀ = epsilon_(zeta₀+1)

epsilon₀ = R₁ H suc 0
epsilon₀ ^ epsilon₀ = R₁ H (R₁ H) suc 0
epsilon₁ = epsilon₀ ^ … ^ epsilon₀ = R₁ (R₁ H) suc 0 = lim suc 0, R₁ H suc 0, R₁ H (R₁ H) suc 0, …
epsilon₀+1 = suc (R₁ H suc 0)
w^(epsilon₀+1) = [suc→H,0→suc] (epsilon₀+1) 0 = H (R₁ H H suc) 0 = H (R₁ H suc) 0
w^w^(epsilon₀+1) = H (R₁ H) H suc 0
w^w^w^(epsilon₀+1) = H (R₁ H) H H suc 0
w^...^w^(epsilon₀+1) = H (R₁ H) H … H suc 0
H (R₁ H) H … H suc 0 = R₁ (R₁ H) suc 0
R₁ (R₂ R₁ H) R₁ H … R₁ H suc 0 = R₂ R₁ (R₂ R₁ H) suc 0 ?

epsilon₀ = R₁ H suc 0
epsilon₁ = R₁ (R₁ H) suc 0
epsilon_a = [suc→R₁, 0→H] (1+a) suc 0
zeta₀ = R₂ R₁ H suc 0
zeta₀+1 = suc (R₂ R₁ H suc 0)
epsilon_(zeta₀+1) = R₁ (R₂ R₁ H R₁ H) suc 0 = R₁ (R₂ R₁ H) suc 0
epsilon_epsilon_(zeta₀+1) = R₁ (R₂ R₁ H) R₁ H suc 0
zeta₁ = epsilon_..._epsilon_(zeta₀+1) = R₁ (R₂ R₁ H) R₁ H … R₁ H suc 0 = R₂ R₁ (R₂ R₁ H) suc 0 ?
zeta_a = [suc→R₂ R₁, 0→H] (1+a) suc 0
zeta₀ = [suc→R₂ R₁, 0→H] (suc 0) suc 0 = R₂ R₁ H suc 0
zeta₁ = [suc->R₂ R₁, 0→H] (suc (suc 0)) suc 0 = R₂ R₁ (R₂ R₁ H) suc 0
zeta_zeta₀ = R₂ R₁ H (R₂ R₁) H suc 0
eta₀ = R₂ (R₂ R₁) H suc 0

epsilon₀ = phi(1,0) = R₁ H suc 0
zeta₀ = phi(2,0) = R₂ R₁ H suc 0
eta₀ = phi(3,0) = R₂ (R₂ R₁) H suc 0
phi(w,0) = R₁ R₂ R₁ H suc 0
phi(1+a,0) = [suc→R₂, 0→R₁] a H suc 0
phi(1,0) = R₁ H suc 0
phi(phi(1,0),0) = [suc→R₂, 0→R₁] phi(1,0) H suc 0 = R₁ H R₂ R₁ H suc 0
phi(…,0) = R₁ H R₂ R₁ H R₂ R₁ H suc 0
Gamma₀ = phi(Gamma₀,0) = phi(1,0,0) = R₃ R₂ R₁ H suc 0

w = phi(1) = H suc 0 = w
epsilon₀ = phi(1,0) = R₁ H suc 0 = Next w
zeta₀ = phi(2,0) = R₂ R₁ H suc 0 = [0] Next w
Gamma₀ = phi(1,0,0) = R₃ R₂ R₁ H suc 0 = [1] [0] Next w
SVO = R_w...1 H suc 0 ?
ou LVO = R₄ R₃ R₂ R₁ H suc 0 = [2] [1] [0] Next w
BHO = R_w...1 H suc 0 ?

Fix f z = f^w (z+1) = H f (suc z)
Next = Fix [w^*]
[0] f = Fix [f^* 0]
phi(1,0) = epsilon₀ = Next 0 = Next w = R₁ H suc 0
phi(1,a) = epsilon_a = Next^(1+a) 0 = Next^(1+a) w = [suc→R₁, 0→H] (1+a) suc 0
phi(2,0) = zeta₀ = epsilon_..._epsilon₀ = (0] Next 0 = Fix [Next^* 0] 0 = H [Next^* 0] 1 = lim
Next 0 = epsilon₀ = R₁ H suc 0
Next^epsilon₀ 0 = epsilon_epsilon₀ = R₁ H R₁ H suc 0
= R₂ R₁ H suc 0
phi(2,1) = zeta₁ = epsilon_...epsilon_(zeta₀+1) = ([0] Next)² 0 = lim
suc (R₂ R₁ H suc 0)
R₁ (R₂ R₁ H R₁ H) suc 0 = R₁ (R₂ R₁ H) suc 0
R₁ (R₂ R₁ H) R₁ H suc 0
= R₁ (R₂ R₁ H) R₁ H … R₁ H suc 0
= R₂ R₁ (R₂ R₁ H) suc 0 ?
= (R₂ R₁)² H suc 0
phi(2,a) = zeta_a = [suc → R₂ R₁, 0→H] (1+a) suc 0
zeta_zeta₀ = [suc → R₂ R₁, 0 → H] (suc (R₂ R₁ H suc 0)) suc 0 = R₂ R₁ (R₂ R₁ H (R₂ R₁) H) suc 0
zeta_zeta_zeta₀ = R₂ R₁ (R₂ R₁ H (R₂ R₁) H) (R₂ R₁) H suc 0
zeta_..._zeta₀ = R₂ R₁ (R₂ R₁ H (R₂ R₁) H) (R₂ R₁) H … (R₂ R₁) H suc 0

( e = epsilon )
e₀ = R₁ H suc 0
w^(e₀ + 1) = [suc→H, 0→suc] (suc (R₁ H suc 0)) 0 = H (R₁ H H suc) 0 = H (R₁ H suc) 0 = e₀ * w
w^w^(e₀ + 1) = w^(e₀ * w) = H (R₁ H H) suc 0 = H (R₁ H) suc 0 = e₀^w
R₁ H (R₁ H suc) 0 = e₀²
H (R₁ H) suc 0 = e₀^w
w^w^w^(e₀ + 1) = w^e₀^w = H (R₁ H) H suc 0 = lim
H suc 0 = w
R₁ H H suc 0 = R₁ H suc 0 = e₀
R₁ H (R₁ H H) suc 0 = R₁ H (R₁ H) suc 0
R₁ H (R₁ H (R₁ H H)) suc 0 = R₁ H (R₁ H (R₁ H)) suc 0
e₀ = R₁ H suc 0
e₀² = R₁ H (R₁ H suc) 0
e₀^a = [suc->R₁ H, 0→suc] a 0
e₀^w = [suc→R₁ H, 0→suc] (H suc 0) 0 = H (R₁ H) suc 0

e₀^e₀^w = H (R₁ H) (R₁ H) suc 0 = lim
R₁ H suc 0
R₁ H (R₁ H) suc 0
R₁ H (R₁ H (R₁ H)) suc 0
e₀^e₀^e₀^w = H (R₁ H) (R₁ H) (R₁ H) suc 0

e₀⁰ = suc 0
e₀ = R₁ H suc 0
e₀^e₀ = R₁ H (R₁ H) suc 0
e₀^e₀^e₀ = R₁ H (R₁ H) (R₁ H) suc 0
… R₁ (R₁ H) suc 0

R'₁ f g = lim f, f g, f g g, …
R₁ = R'₁ I
R'₁ I (R'₁ I H) suc 0 = R'₁ (H (R'₁ I H)) H suc 0 ?

w^w^(e0+1) = e0^w
w^w^w^(e0+1) = e0^e0^w
supp. W^...^w^w^(e0+1) = e0^...^e0^w
dem w^...^w^w^w^(e0+1) = e0^...^e0^e0^w
e0^...^e0^w = (w^e0)^e0^...^e0^w = w^(e0*e0^...^e0^w) = w^e0^(1+e0^...(n-1)...^e0^w = w^e0^...^e0^w = w^w^...^w^(e0+1)

w^w^(e0+1) = e0^w
e0 = R1 H suc 0
w^a = [suc→H,0→suc] a 0
w^(e0+1) = [suc→H,0→suc] (suc (R1 H suc 0)) 0 = H (R1 H H suc) 0 = H (R1 H suc) 0
w^w^(e0+1) = H (R1 H H) suc 0 = H (R1 H) suc 0
e0^a = [suc→R1 H, 0→suc] a 0
e0^w = [suc→R1 H, 0→suc] (H suc 0) 0 = H (R1 H) suc 0
w^w^w^(e0+1) = H (R1 H) H suc 0
e0^e0^w = H (R1 H) (R1 H) suc 0
supp H (R1 H) H … H suc 0 = H (R1 H) (R1 H) … (R1 H) suc 0
dem H (R1 H) H H … H suc 0 = H (R1 H) (R1 H) (R1 H) … (R1 H) suc 0
e0 = R1 H suc 0
w^e0 = [suc→H, 0→suc] (R1 H suc 0) 0 = (R1 H H suc) 0 = R1 H suc 0
H (R1 H) H H … H suc 0 = lim
H H … H suc 0
R1 H H H … H suc 0
R1 H (R1 H H) H … H suc 0 = R1 H (R1 H) H … H suc 0
H (R1 H) (R1 H) (R1 H) … (R1 H) suc 0 = lim
R1 H (R1 H) … (R1 H) suc 0
R1 H (R1 H) (R1 H) … (R1 H) suc 0
R1 H (R1 H (R1 H)) (R1 H) … (R1 H) suc 0
R1 (R2 R1 H) R1 H … R1 H suc 0 = R2 R1 (R2 R1 H) suc 0 ?
H (R1 H) H … H suc 0 = R1 (R1 H) suc 0 = (R1 H) … (R1 H) suc 0 = H (R1 H) (R1 H) … (R1 H) suc 0
R1 (R2 R1 H) R1 H … R1 H
R2 R1 (R2 R1 H) suc 0
= R1 (R2 R1 H) R1 (R2 R1 H) … R1 (R2 R1 H) suc 0
phi(2,1) = zeta1 = e_..._e_(zeta0+1)
e_a = [suc→R1,0→H] (1+a) suc 0
zeta₀ = R2 R1 H suc 0
zeta₀ + 1 = suc (R2 R1 H suc 0)
e_(zeta_0+1) = R1 (R2 R1 H R1 H) suc 0 = R1 (R2 R1 H) suc 0
e_e_(zeta_0+1) = R1 (R2 R1 H) R1 H suc 0
e_e_e_(zeta_0+1) = R1 (R2 R1 H) R1 H R1 H suc 0
…
R1 (R2 R1 H) R1 H … R1 H suc 0
= R2 R1 (R2 R1 H) suc 0 ?

phi(2,0) = zeta₀ = R2 R1 H suc 0
zeta₀ ^ … ^zeta₀ = w^...^w^(zeta₀ + 1)
R2 R1 H suc (R2 R1 H suc 0) = zeta₀ * 2
R2 R1 H (R2 R1 H) suc 0 = zeta₀ ^zeta₀
R1 (R2 R1 H) suc 0 = zeta₀ ^… ^zeta₀ = w^...^w^(zeta₀+1)
R1 (R1 (R2 R1 H)) suc 0 = e_(zeta₀+1)^...^e_(zeta₀+1) = w^...^w^(e_(zeta₀+1)+1) = e_(e_(zeta₀+1)+1)
… H R1 (R2 R1 H) suc 0 = lim
R2 R1 H suc 0 = zeta₀
R1 (R2 R1 H) suc 0 = zeta₀ ^ … ^ zeta₀ = w^...^w^(zeta₀ + 1) = e_(zeta₀ + 1)
R1 (R1 (R2 R1 H)) suc 0
= H [e_(*+1)] zeta₀
a^...^a^w = w^...^w^w^(a+1) → e_(a+1)
a^...^a = w^...^w^(a*2)
H R1 (R2 R1 H) suc 0
R1 H R1 (R2 R1 H) suc 0
R1 (R2 R1 H) R1 (R2 R1 H) suc 0
R2 R1 (R2 R1 H) suc 0
H (R2 R1) H suc 0
(R2 R1) H (R2 R1) H suc 0
R2 (R2 R1) H suc 0
H R2 R1 H suc 0
R2 R1 H R2 R1 H suc 0
R3 R2 R1 H suc 0

phi(1,0) = e0 = R1 H suc 0
phi(2,0) = z0 = R2 R1 H suc 0
phi(2,1) = z1 = R1 (R2 R1 H) R1 H … R1 H suc 0 = R2 R1 (R2 R1 H) suc 0 ?
phi(2,a) = (R2 R1)⁽1+a) H suc 0 ?
phi(2,w) = H (R2 R1) H suc 0
phi(2,phi(2,0)) = R2 R1 H (R2 R1) H suc 0
phi(3,0) = R2 (R2 R1) H suc 0
phi(1+a,0) = R2^a R1 H suc 0
phi(phi(1,0),0) = R1 H R2 R1 H suc 0
phi(1,0,0) = R3 R2 R1 H suc 0 = Gamma0
R3 R2 R1 H suc (R3 R2 R1 H suc 0) = Gamma0 * 2
R3 R2 R1 H (R3 R2 R1 H suc) 0 = Gamma0 ^ 2
R3 R2 R1 H (R3 R2 R1 H) suc 0 = Gamma0 ^Gamma0
Gamma0 ^ a = [suc→R3 R2 R1 H, 0→suc] a 0
R1 (R3 R2 R1 H) suc 0 = Galla0 ^ … ^ Gamma0 = w ^ … ^ w ^ (Gamma0+1) = w ^ … ^ w ^ (Gamma0*2) = e_(Gamma0+1) = phi(1,Gamma0+1) = phi(1,0,1)
phi(1,0,0) = R3 R2 R1 H suc 0
phi(1,0,1) = R1 (R3 R2 R1 H) suc 0
phi(1,0,a) = [suc→R1, 0→R3 R2 R1 H] a suc 0
phi(1,0,phi(1,0,0)) = R3 R2 R1 H R1 (R3 R2 R1 H) suc 0
phi(1,1,0) = R2 R1 (R3 R2 R1 H) suc 0
phi(1,a,0) = (R2 R1)^a (R3 R2 R1 H) suc 0
phi(1,phi(1,0,0),0) = R3 R2 R1 H (R2 R1) (R3 R2 R1 H) suc 0
phi(2,0,0) = R2 (R2 R1) (R3 R2 R1 H) suc 0
phi(phi(1,0,0),0,0) = R3 R2 R1 H (R2 (R2 R1)) (R3 R2 R1 H) suc 0
phi(1,0,0,0) = R2 (R2 (R2 R1)) (R3 R2 R1 H) suc 0

w = phi(1) = H suc 0
e0 = phi(1,0) = R1 H suc 0
z0 = phi(2,0) = R2 R1 H suc 0
GammaO = phi(1,0,0) = R3 R2 R1 H suc 0
phi(1,0,0,0) = R2 (R2 (R2 R1)) (R3 R2 R1 H) suc 0 ?

https://johncarlosbaez.wordpress.com/2016/07/07/large-countable-ordinals-part-3/

récapitulation
w^a = [suc:H,0:suc] a 0
e0^a = [suc:R1 H,0:suc] a 0
e_a = [suc:R1,0:H] (1+a) suc 0
z_a = suc:H R1,0:R2 R1 H] a suc 0
a^...^a = w^...^w^(a+1) = e_(a+1)
w^...^w^(e0+1) = H (R1 H) H … H suc 0 = e0^...^e0 = R1 (R1 H) suc 0
a = f suc 0 => a^a = f f suc 0, … , a^...^a = e_(a+1) = R1 f suc 0

phi(1,0) = e0 = R1 H suc 0
phi(2,0) = z0 = R2 R1 H suc 0
phi(2,1) = z1 = e_..._e_(z0+1) = R1 (R2 R1 H) R1 H … R1 H suc 0 = R2 R1 (R2 R1 H) suc 0 ? ou H R1 (R2 R1 H) suc 0 ?

R2 R1 H suc 0 = z0
R1 (R2 R1 H) suc 0 = z0^...^z0 = e_(z0+1) = [suc:R1,0:H] (suc (R2 R1 H suc 0)) suc 0 = R1 (R2 R1 H R1 H) suc 0 = R1 (R2 R1 H) suc 0
R1 (R1 (R2 R1 H)) suc 0 = e_(z0+1)^...^e_(z0+1) = e_(e_(z0+1)+1)
H R1 (R2 R1 H) suc 0 = e_...e_(z0+1)+1...+1 = ? e_...e_z0+1 = z1
R1 (H R1 (R2 R1 H)) suc 0 = z1^...^z1 = e_(z1+1) = [suc:R1,0:H] (suc (RH R1 (R2 R1 H) suc 0)) suc 0 = R1 (H R1 (R2 R1 H) R1 H) suc0
H R1 (H R1 (R2 R1 H)) suc 0 = e_...e_(z1+1)...+1 = ? e_...e_z1+1 = z2 = phi(2,2)
phi(2,a) = z_a = ? [suc:H R1,0:R2 R1 H] a suc 0
z₀ = R2 R1 H suc 0
z_z₀ = R2 R1 H (H R1) (R2 R1 H) suc0
z_z_z0 = R2 R1 H (H R1) (R2 R1 H) (H R1) (R2 R1 H) suc 0
phi(3,0) = eta₀ = R2 (H R1) (R2 R1 H) suc 0

R3 R2 R1 H suc 0
R2 R1 H R2 R1 H suc 0
R1 H R1 H R2 R1 H suc 0
H H R1 H R2 R1 H suc 0
H (H R1) H R2 R1 H suc 0
H R1 (H R1 H) R2 R1 H suc 0
R1 (R1 (H R1 H)) R2 R1 H suc 0
R1 (H R1 H) (R1 (H R1 H)) R2 R1 H suc 0
H R1 H (H R1 H) (R1 (H R1 H)) R2 R1 H suc 0
R1 (R1 H) (H R1 H) (R1 (H R1 H)) R2 R1 H suc 0
R1 H (R1 H) (H R1 H) (R1 (H R1 H)) R2 R1 H suc 0
H H (R1 H) (H R1 H) (R1 (H R1 H)) R2 R1 H suc 0
H (H (R1 H)) (H R1 H) (R1 (H R1 H)) R2 R1 H suc 0
H (R1 H) (H (R1 H) (H R1 H)) (R1 (H R1 H)) R2 R1 H suc 0
R1 H (R1 H (H (R1 H) (H R1 H))) (R1 (H R1 H)) R2 R1 H suc 0

A faire :

étudier psi Buchholz

séquences fondamentales et programmes pour :
 phi étendu
 theta
 C Taranovsky

correspondance notation combinatoire

table : ajouter theta et C Taranovsky

nouvelle version latex

Schütte's Klammersymbols, Schütte bracket :

http://www.mathematik.uni-muenchen.de/~buchholz/articles/jaegerfestschr_buchholz3.pdf

http://www.cs.man.ac.uk/~hsimmons/TEMP/OrdNotes.pdf

Ordinal collapsing functions :

https://en.wikipedia.org/wiki/Ordinal_collapsing_function

http://googology.wikia.com/wiki/Ordinal_notation

http://quibb.blogspot.fr/2012/03/infinity-impredicative-ordinals.html

http://web.mit.edu/dmytro/www/other/OrdinalNotation.htm

Autres représentations :

http://log.chez.com/text/logic/transfinite-notations.htm

http://www.madore.org/~david/math/ordtrees.pdf

Transfinite iteration of reflection principle

http://www.phil.uu.nl/~jjoosten/events/SeminariCuc/Slides/SeminariCucDuque.pdf